## Slide 1: MIK performance at the MAX IV 3 GeV ring and beam dynamics of a MIK for the MAX IV 1.5 GeV ring
Marco Apollonio
MAX IV Laboratory, Lund, Sweden
3rd workshop on low-emittance lattice design
ALBA – Barcelona, June 2022

## Slide 2: foreword and layout – why a Multipole Injection Kicker?
reducing the transient stored beam perturbation during (frequent) top-up injections
more and more relevant when moving towards 4th generation low emittance machines
Engineering design by SOLEIL (2012-2017)
  Prototype installed 2017
  Final version since 2019
MIK design and commissioning for the 3 GeV ring
performance:
  high injection efficiency
  high “transparency”
porting the concept to the 1.5GeV ring
  beam dynamics studies
  state of the project
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 3: MAX IV complex
MAX IV SR in numbers |  | 
ring | R3 | R1
lattice type | 7BA – 20 achromats | DBA – 12 achromats
energy (GeV) | 3.0 | 1.5
L (m) / T (ms) | 528 / 1.76 | 96 / 0.32
Ibeam (mA) | 300 | 400
top-up interval (min) | 10 | 30
nx,y | 44.20 / 16.28 | 11.22 / 3.15
xx,ynat | -49.9 / -50.0 | -24.9 / -16.6
ex / ey (pm rad) | 330* / 8 | 5900* / 27
(*) bare lattice
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 4: MAX IV complex
DK
MIK
3.0 GeV ring
septum
MIK
DK
Vertical Transfer Lines
1.5 GeV ring
DK
septum
DK
MIK
new MIK

## Slide 5: MAX IV complex
Storage Ring INJECTION |  | 
 | R3 – 3.0 GeV | R1 – 1.5 GeV
Septum inner / outer wall | -10.0mm / -12.5mm | -13.5mm / -16.0mm
Vertical Extraction Septum bending angle | 5o | 10o
Injection Point (end of septum magnetic field) | 1.90m (from injection straight mid-point) | 1.25m (from injection straight mid-point)
Nominal Injection position (horizontal plane) | -13.5mm | -17.0mm
Present Injection Kicker | Multipole Injection Kicker (28.3m from injection straight mid-point) | Dipole Kicker (14.8m from injection straight mid-point)
Complementary device | Dipole Kicker (5.04m from injection straight mid-point) | -
Future Injection Kicker | - | Multipole Injection Kicker (15.7m from injection straight mid-point)
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 6: MIK main characteristics
top-up injection [1] of the e-beam into the storage ring without disturbance on stored beam
8 copper rods [2] form the octupole field with “zero” field region at the position of the stored beam
precisely machined monocrystal sapphire ceramic chamber to insure the accurate copper rods positioning
titanium coating of few μm-thick inner surface of the vacuum chamber (image current)
few μs, half sine signal, generated by pulser with repetition rate of up to 10 Hz.
MIK cross-section showing the copper rods positions
Integrated magnetic field distribution, expressed as a deflection angle of the 3.0 GeV e-beam
M. Apollonio, LEL-III, ALBA, Barcelona, 2022
[2] T. Atkinson, M. Dirsat, O. Dressler, P. Kuske, H. Rast, Development of a non-linear kicker system to facilitate a new injection scheme for the Bessy-II storage ring, in:
IPAC 2011 - 2nd International Particle Accelerator Conference, ISBN:9789290833666, 2011, pp. 3394–3396.
[1] Patrick Alexandre, Rachid Ben El Fekih, Antoine Letrésor, Serge Thoraud, José da Silva Castro, François Bouvet, Jonas Breunlin, Åke Andersson, and Pedro Fernandes Tavares, Transparent top-up injection into a fourth-generation storage ring,
Nuclear Inst. and Methods in Physics Research, A 986, 164739 (2021).
20mm
14mm
46.8mm
7.8mm
R3 (3GeV) - MIK details | 
bx / by (MIK) | 9.4 / 3.8 m
bx / by (ID long str.) | 9 / 2 m
Injected beam position @MIK (x, y) | (-4.665, 0) mm
MIK deflection angle | -1.176 mrad
LMIK | 30 cm
Nominal pulse duration (half-sine w.f.) | 3.5 ms
Nominal rep. rate | Up to 10 Hz
Integrated Field at inj. Beam position | 11.7 x mT.m
Horiz. / Vert. BSC | 46.8 / 7.8 mm
Peak current (max voltage) | 7kA (15kV)

## Slide 7: Horizontal Beam Dynamics during MIK injection
LINAC emittance @ R3 injection
eX = 1.7 nm / bX = 9.2m
sX = 125 mm
LINAC emittance @ R1 injection
eX = 3.4 nm / bX = 6.2m
sX = 145 mm
Twiss Parameters of 3GeV ring
Twiss Parameters of 1.5GeV ring

## Slide 8: MIK main characteristics – SOLEIL measurements
2D measured map of the integrated field [Internal Short Note on MAXIV MIK-2, Magnetic Measurement Report 13/3/2019, Soleil]
MIK introduced as a KickMap in the AT model
With a beam crossing at -8.55mm and a reduced beam rigidity, MIK@R1 imparts a kick of -2.75mrad with a peak current of about 2.3kA
With a beam crossing at -4.665mm MIK@R3 imparts a kick of 1.17mrad This corresponds a current of about 7kA

## Slide 9
MIK @ R3 – 3GeV
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 10: Horizontal Beam Dynamics during MIK injection
no-kick: beam lost
injected beam
AT-model
propagated beam
crossing @MIK crucially defines kick effectiveness
small beam size important to reduce kick spread
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 11: MIK @3.0 GeV ring: MAX IV-Soleil collaboration (2012-2017, 2019)
MIK @ 3.0GeV ring main parameters | 
Integrated field strength (3.0 GeV, Xinj=-4.66 mm, -1.176 mrad) | -11.7 mTm
Pulse duration / Repetition rate | 3.5 µs / up to 10Hz
Pulse peak current | 7 kA @Umax=15 kV
MIK magnet/vacuum chamber installed in 3.0 GeV Ring
prototype installed and successfully commissioned in 3.0 GeV ring (2017) / backup system – Dipole Kicker (BINP)
Chamber #1(Prototype)
coating thickness=0.8 µm  max. measured
surface temperature@250 mA beam= 75°C
replaced by the new chamber #2(final version) in summer 2019
coating thickness 3.5 µm 
max. measured surface temperature@ 250mA
beam =47°C
precise positioning of the copper rods 
better field quality (wider “zero” field region)
10 temperature probes on sapphire chamber
M. Apollonio, LEL-III, ALBA, Barcelona, 2022
Courtesy of A. Vorozhstov, MAC 11-12-2021, MAX IV

## Slide 12: MIK @3.0 GeV ring: performance – stored beam transparency
e.g. within 433 mm stored beam inflation less tan 10%
Map of iso-inflation of the beam size for an ideal MIK with (x0, y0) position shifts
M. Apollonio, LEL-III, ALBA, Barcelona, 2022
MIK octupolar field outperforms a pulse sextupole injector (originally thought [3] for MAX IV – R3)
[3] S. C. Leemann, Pulsed sextupole injection for Sweden’s new light source MAX IV, Phys. Rev. ST Accel. Beams 15, 050705 – Published 8 May 2012

## Slide 13: MIK @3.0 GeV ring: performance – stored beam transparency
effect of rod mis-alignments
d = 20 mm displacement
20 mm (x,y) RMS
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 14: MIK @3.0 GeV ring: performance – measured residuals
measured residual perturbation map
Identifying optimal working point
minimal perturbation on Stored Beam
scan in (X,Y) while pulsing MIK (2019 final device)
beam size measured by Diagnostic BL synchronized with MIK pulse
camera integration time: compromise between fast acquisition and good S/N
TbT data from 40 + 40 BPMs
Measurement Details
3mA
bunch train (10 bunches) < 100ns
  kick almost uniform within 0.1%
Initial coarse scan with single CM
  MIK re-aligned by
  (-600 mm, -500 mm)
  finer scans w. closed bumps
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 15: MIK @3.0 GeV ring: performance – MIK “transparency”
Vertical stored beam size change caused by pulsing the MIK, 𝛿𝜎𝑦=0.6±0.1 𝜇𝑚
slow camera acquisition: 4.4ms (2500 turns)
fast camera acquisition: 0.25ms (150 turns)
“MIK transparency”
beam size variation when operating the kicker
(sub)-mm H/V beam size variation achieved
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 16: MIK @3.0 GeV ring: performance – measured damping times
measured damping times
diag. camera synch’d to acquire at given delay w.r.t. MIK pulse trigger
t (ms)
MIK pulse
(t=tK)
tyth = 29ms
txth = 16ms
M. Apollonio, LEL-III, ALBA, Barcelona, 2022
NB: beam moved out of soft spot to enhance signal

## Slide 17: MIK @3.0 GeV ring: performance – injection efficiency
injection efficiency [1] between 92 and 94% (improving at larger currents)
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 18
MIK @ R1 – 1.5GeV
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 19
porting the MIK injector to the 1.5 GeV ring
R1 (1.5 GeV) - MIK details | 
bx / by (MIK) | 6.2 / 3.8 m
bx / by (ID long str.) | 5.99 / 2.87 m
Injected beam position @MIK (x, y) | (-8.55, 0) mm
MIK deflection angle (1st) – double shot | S1: +2.75 mrad S2: +2.40 mrad
LMIK | 30 cm
Nominal pulse duration (half-sine w.f.) | 1.28 ms
Nominal rep. rate | Up to 10 Hz
Integrated Field at inj. Beam position | +13.7 mT.m
Horiz. / Vert. BSC | 46.8 / 7.8 mm
Peak current (max voltage) | 5kA (24kV)
M. Apollonio, LEL-III, ALBA, Barcelona, 2022
NB: MIK@R1 more challenging than @R3
Large peak current
Shorter pulse
Double kick
project to implement transparent injection into the 1.5 GeV Ring started in 2021

## Slide 20
MIK @1.5 GeV ring: injection dynamics [3]
Matlab-AT model
M. Apollonio, LEL-III, ALBA, Barcelona, 2022
Courtesy of A. Vorozhstov,
MAC 11-12-2021, MAX IV
[Internal Short Note on MAXIV MIK-2, Magnetic Measurement Report 13/3/2019, Soleil]
MIK kick map
[4] M. Apollonio, Å. Andersson, M. Brosi, D. K. Olsson, P. F. Tavares, A. S. Vorozhstov, Beam Dynamics of the Transparent Injection for the MAX IV 1.5 GeV Ring, In Proc. IPAC22, MOPOPT022
+2.75mrad
-0.87mrad

## Slide 21: MIK @1.5 GeV ring: optimisation
Parameter scan on transfer line exit angle and MIK peak current: (x’inj, Ibeam)
Full optimization on transfer line parameters and MIK peak current: (xinj, x’ inj, Ibeam)
Courant-Snyder invariant compression
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 22: MIK @1.5 GeV ring: real machine acceptance
Machine test to assess real acceptance prior to installation of the device
Stored beam excited with DK at growing voltages (kicking angles)
Beam current sudden drop at qDK = 2.18 mrad
Simulation with DK injection predicts injected beam touches septum inner wall at about the same kicking angle
This corresponds to A = 29 mm.mrad, well above the 11.5 mm.mrad needed for solution S1
Conclusion: no evident issue to install MIK in straight-3
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 23: CONCLUSIONS
R3 - MIK
MAX IV installed and commissioned a MIK prototype in 2017
Swapped (2019) with a better and fully operating a MIK (top-up period 10min)
Designed/built at SOLEIL
  pure crystalline sapphire chamber (Kyocera)
  machining and rod-positioning crucial for field definition
  Ti-coating thickness important to reduce temperature in operation
Injection Efficiency at large current: >94% (commissioning) / >90% (today)
Sub-mm transparency
Anecdotical feedback of good performance from beamlines
  No BL using gating / no issue claimed / happy with top-up interval (30min  10min)
R1 - MIK
Design closely following MIK @R3, although we will operate with a shorter pulse
  two-turn kick due to short length of R1
R3 prototype device ready to be installed  summer shutdown
  2 spare chambers considered
pulser / electronics for control may undergo some delay
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 24
Thanks for your attention …
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 25
… spares
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 26: MIK @3.0 GeV ring: performance – control of temperatures
MIK ceramic temperatures at 250mA multi-bunch mode
tolerance: 120 oC
Prototype 2017 – Ti thickness: 0.8 mm
T = [55, 75] oC
Final Chamber 2019 – Ti thickness: 3.5 mm
T = [35, 48] oC
analysis of effects of eddy currents
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 27: MIK @1.5 GeV ring: tune resilience
Studies show that a simulated injection with the MIK for chosen optimized solution (e.g. S1) is unaffected by horizontal tune variations between 11.19 and 11.37
Tune shifts may be a either a deliberate choice or e.g.the result of non completely compensated variations of ID gaps.
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 28: MIK @1.5 GeV ring: stored beam transparency
effect of rod mis-alignments (preliminary): one rod moved by 50mm
Beam inflation less pronounced than the low-emittance case
MIK @R1 less demanding in mechanical tolerance
M. Apollonio, LEL-III, ALBA, Barcelona, 2022

## Slide 29
M. Apollonio, LEL-III, ALBA, Barcelona, 2022