## Slide 1: Cherenkov Diffraction Radiation as a potential Beam size measurement technique
M. Bergamaschi1, V.V. Bleko2, M. Billing3, L. Bobb4, J. Conway3, R. Kieffer1, A.S. Konkov2 P. Karataev5, R.O. Jones1, T. Lefevre1, J.S. Markova2, S. Mazzoni1, Y. Padilla Fuentes3, A.P. Potylitsyn2, J. Shanks3
1. CERN, Geneva, Switzerland 2. Tomsk Polytechnic University, Tomsk, Russia 3. Cornell University, Ithaca, New York, USA 4. Diamond Light Source, Oxfordshire, United Kingdom 5. John Adams Institute at Royal Holloway, University of London, Egham, United Kingdom

## Slide 2: Outline
Development of non-invasive beam size monitor for CLIC
  From the emission of Diffraction radiation in Slits to Cherenkov Diffraction Radiation in longer dielectric
Experimental set-up on CESR
Experimental results obtained in 2017
Perspectives and outlook for beam instrumentation
M. Bergamaschi, TWEMLSF, ALBA

## Slide 3: Motivation to develop Incoherent Cherenkov Diffraction Radiation
Ref: A.P. Potylitsyn et al, Diffraction radiation from charged particles, STMP 29 (Springer Berlin Hedeilberg 2010)
Suppress Synchrotron radiation  cleaner signal
  DR and SR are emitted at similar angles
  Looking for a physical process emitted at larger angles
Larger aperture slits (>500 um)
  Difficult as DR will provide less photons
  Looking for a physical process providing more photons
‘Generating Cherenkov diffraction radiation in longer dielectric’
M. Bergamaschi, TWEMLSF, ALBA

## Slide 4: Incoherent Cherenkov Diffraction Radiation
Incoherent Cherenkov Diffraction Radiation (ChDR)
The electric field of ultra-relativistic charged particles passing in the vicinity of a dielectric radiator produce photons by Cherenkov mechanism (polarization effect).
Large emission angle:
Photons emitted along the target
For a cylindrical geometry
L
Exponential decay
of the particle field
a, fine structure constant
b, normalised beam velocity
g, beam relativistic factor
q, angle of observation
Cherenkov emission
Ref: A.P. Potylitsyn et al, Diffraction radiation from charged particles, STMP 29 (Springer Berlin Hedeilberg 2010)
h
Cherenkov DR
photons
Dielectric
E Field
Vacuum
M. Bergamaschi, TWEMLSF, ALBA

## Slide 5: Experimental set-up on CESR (1/2)
One bunch
2.5nC
ChDR
Target
Camera
ChDR
Re-using the DR vacuum chamber and optical system
M. Bergamaschi, TWEMLSF, ALBA

## Slide 6: Experimental set-up on CESR (2/2)
Design a 2cm long SiO2 (n=1.46) Cherenkov Diffraction Radiation target
  Testing with 5.3GeV e- / e+ and measuring in visible (0.3-0.7um) – October 2017
  Testing with 2.1GeV e- and measuring in IR (0.9-1.7um) – April 2017
l= 600±10nm
l= 400±10nm
    M.V. Shevelev and A.S. Konkov, JETP 118, 501 (2014)
M. Bergamaschi, TWEMLSF, ALBA
‘The red curve as been scaled down by 1/3 for better presentation

## Slide 7
Two different geometries have been tested
  Prismatic radiator
  Flat radiator (simpler and cheaper)
Cherenkov radiators
Prismatic target for polarization studies
M. Bergamaschi, TWEMLSF, ALBA

## Slide 8: Experimental data : Positron at 5.3GeV
Horizontal polarization
Vertical polarization
Positron Beam
Cherenkov
Diffraction
Radiation
Positron Beam
‘Vertically polarized photons give the best spatial resolution (sy=2mm)’
M. Bergamaschi, TWEMLSF, ALBA
Measuring the horizontal Beam size :

## Slide 9: Experimental data : Electron at 2.1GeV
Steering the beam vertically
  No wavelength filter – no polarizer
‘Cherenkov photons yield increasing strongly for smaller impact parameter’
M. Bergamaschi, TWEMLSF, ALBA

## Slide 10: Experimental data : Positron at 5.3GeV
ChDR @600±10nm ; hmean = 1.5mm
‘Measuring the Beam tilt angle with respect to the surface of dielectric
as the light intensity strongly depends on the impact parameter’
Rotating the target :
Positrons
Target angle, a
1.5mm
350um
a = 4.28 deg (74mrad)
a = 0.98 deg (17mrad)
l= 600nm
M. Bergamaschi, TWEMLSF, ALBA

## Slide 11: Experimental data : Measuring counter-propagating beams
Measuring counter-propagating beams using the prismatic target
(a)
M. Bergamaschi, TWEMLSF, ALBA

## Slide 12: Experimental data : Measuring counter-propagating beams
Imaging both beams with the prismatic target
(a)
Electron Beam
Cherenkov
Diffraction
Radiation
Electron Beam
The photons produced by electrons and positrons appear on a different part of the target and give the possibility to high directivity beam measurements (measured more than 60dB)
Positron Beam
Cherenkov
Diffraction
Radiation
Positron Beam
Images from e- is truncated due to the limited aperture of the current detection system
M. Bergamaschi, TWEMLSF, ALBA

## Slide 13: Summary
Incoherent ChDR has been studied in IR and visible range for beams propagating at a distance of 1-3mm from the edge of the dielectric
The light is polarized and emitted in a narrow cone angle, different from SR angle providing excellent S/N ratio
The number of photons scales linearly with the length of the radiator and exponentially with the impact parameter
  e.g. for 5.3GeV and h=1.5mm, measured 10-3 photons/turn/particle
Qualitative concept proved for mm beam size
M. Bergamaschi, TWEMLSF, ALBA

## Slide 14: Perspectives for beam instrumentation
Imaging system for relativistic beam
  What is the the smallest beam size measurable ?
    The Cherenkov diffraction PSF should be smaller than transition radiation PSF
   possible tests in 2018 with micron beam sizes on ATF2
What is the smallest the beam tilt angle measurable ?
  A non linear response depending on wavelength, beam energy and impact parameter
Measuring counter-propagating beams with very high directivity : BPM for FCC, HE-LHC, …
A Beam Position Monitor for Crystal collimator on LHC
A Beam Position Monitor in Dielectric Wakefield acceleration
M. Bergamaschi, TWEMLSF, ALBA

## Slide 15: Thanks for your attention
M. Bergamaschi1, V.V. Bleko2, M. Billing3, L. Bobb4, J. Conway3, R. Kieffer1, A.S. Konkov2 P. Karataev5, R.O. Jones1, T. Lefevre1, J.S. Markova2, S. Mazzoni1, Y. Padilla Fuentes3, A.P. Potylitsyn2, J. Shanks3
1. CERN, Geneva, Switzerland 2. Tomsk Polytechnic University, Tomsk, Russia 3. Cornell University, Ithaca, New York, USA 4. Diamond Light Source, Oxfordshire, United Kingdom 5. John Adams Institute at Royal Holloway, University of London, Egham, United Kingdom

## Slide 16: Back-up slides

## Slide 17: Experimental data : Positron at 5.3GeV
Imaging the Flat radiator (diffusive coating to extract the photons out of the target)
Cherenkov
Diffraction
Radiation
Positron
Beam
Positron
Beam
Cherenkov
Diffraction
Radiation
‘Cherenkov photons emitted all along the target surface’
M. Bergamaschi, TWEMLSF, ALBA

## Slide 18
Pictures of the radiators
Depolished
& Coated
Depolished
Area - no coating
Polished
& Coated
T. Lefevre, LER 2018, CERN
Cherenkov radiators (2/2)

## Slide 19: Experimental data : Positron at 5.3GeV
Angular distributions with Prismatic radiator : Comparison with simulations
Measurements
Simulations
Horizontal polarization
Vertical polarization
M. Bergamaschi, TWEMLSF, ALBA

## Slide 20: Incoherent Diffraction Radiation on CESR (4/6)
Offset
Steering the beam through the slit
Conditions: wavelength 400/600 nm, beam size: 16.2/23.7 um, slit width 0.5mm
Different sensitivity depending on the wavelength
T. Lefevre, LER 2018, CERN

## Slide 21
Pictures of the radiators
Depolished
& Coated
Depolished
Area - no coating
Polished
& Coated
Cherenkov radiators (2/2)
M. Bergamaschi, TWEMLSF, ALBA

## Slide 22: Experimental data : Positron at 5.3GeV
Imaging the prismatic target at wavelength of 600±10nm
Positron Beam
Cherenkov
Diffraction
Radiation
Cherenkov
Diffraction
Radiation
Positron Beam

## Slide 23: Experimental data : Positron at 5.3GeV
Steering the beam vertically
  Wavelength 600±10nm
  Vertical Polarization component
h= 0.96mm 1.17mm 1.52mm 2.09mm 2.43mm
Cherenkov photons yield increasing strongly for smaller impact parameter

## Slide 24: Experimental set-up on CESR (2/2)
Design a 2cm long SiO2 (n=1.46) Cherenkov Diffraction Radiation target
  Testing with 5.3GeV e- / e+ and measuring in visible (0.3-0.7um) – October 2017
Gated and intensified camera
l= 600±10nm
l= 400±10nm
    M.V. Shevelev and A.S. Konkov, JETP 118, 501 (2014)
M. Bergamaschi, TWEMLSF, ALBA

## Slide 25: Experimental set-up on CESR (2/3)
Design a 2cm long SiO2 (n=1.46) Cherenkov Diffraction Radiation target
  Testing with 2.1GeV e- and measuring in IR (0.9-1.7um) – April 2017
Xenics Bobcat 640 GigE
Cooled InGaAs 640x512 pixels : 20um pixel pitch
QE up to 80% at 1.6um
14bit ADC
1us-40ms integration window
    M.V. Shevelev and A.S. Konkov, JETP 118, 501 (2014)
‘The red curve as been scaled down by 1/3 for better presentation
M. Bergamaschi, TWEMLSF, ALBA

## Slide 26: Experimental data : Positron at 5.3GeV
Prismatic target : Angular distribution and polarization study
Impact parameter fixed , 600±10nm wavelength, Polarization Scan

## Slide 27: Experimental data : electron at 2.1GeV
Prismatic target for the detection of electrons

## Slide 28: Experimental data : electron at 2.1GeV
Target Movement
Optically polished ChDR target insertion passing over a 3mm de-polished strip on the surface.
Diffusive surface =>We loose the highly directional ChDR emission.
3mm Strip
3mm Strip

## Slide 30: Perspectives on radiator’s shapes and material
ChDR
Beam
Prismatic or flat targets ? Something else ?
  BPM using flat target – possibly using long(er) target
  Imaging system requiring to select the appropriate polarization
How thick should a target be ? cm/mm/um ?
  ChDR is mainly emitted within the first atomic layer of the dielectric since the beam field decreases as it penetrates inside the material
Testing different materials for different applications / wavelength
Silicon
Diamond
M. Bergamaschi, TWEMLSF, ALBA

## Slide 31: Conclusions
Incoherent Cherenkov Diffraction Radiation looks promising for Beam diagnostic applications on both high-energy leptons and hadrons
After CESR, several beam tests prepared at CERN/CLEAR and possibly at KEK/ATF2 and Diamond in order to continue the R&D
Optimisation of the radiator geometry for a given application
  Best shape/configuration for light extraction and polarization selection
Motivation to study the Beam dynamic involved in the emission of ChDR
  ChDR is the emission of wakefield in a dielectric materiel
  Coherent and incoherent emissions should lead to very different beam dynamic effects
  Some work on-going on the simulation/theoretical sides (Tomsk Univ.)
    Simulations of coherent ChDR is being studied with codes such as Particle studio, Magic or Vsim for different applications (Dielectric acceleration and THz source)
M. Bergamaschi, TWEMLSF, ALBA

## Slide 33: ChDR measurements at CERN
Previously named CTF3-CALIFES, the new CERN electron beam test facility CLEAR is being commissioned at present.
Beam: 130-220MeV electrons
Up to 0.5nC per bunch, trains available 1-100 bunches.
CLEAR Proposal online: https://clear.web.cern.ch/sites/clear.web.cern.ch/files/documents/CLEAR_proposal.pdf
End of 2017 two ChDR experiments foreseen, in the infrared range:
  Under vacuum, using CVD diamond radiator.
  In-air, using crystalline silicon radiator.

## Slide 34: 1. Diamond ChDR on CLEAR at CERN
CVD diamond radiator under vacuum.
Goal: Comparison between OTR, Cherenkov, and ChDR light emission.
Already tested cameras on that setup:
Ueye (visible range) =>Nice images, but inappropriate wavelength for diffraction radiation studies at 200 MeV
Onca-MWIR-InSb (2-5um) =>Bad SNR
Gobi-LWIR(8-15um) =>Bad SNR (bolometer)
To be tested soon:
Bobcat-SWIR(0.8-1.6um) Might be the right one for this measurement.
TR screen
ChDR radiator
e- Beam
ChDR
Al coating
h
Ueye
Onca
Gobi
Bobcat
Ueye image

## Slide 35: Experimental set-up at Califes@CERN
CALIFES : 200MeV electrons – up to 15nC per bunch train
15x2x1.2mm Diamond crystal with one face cut and Al Coated to reflect the ChDR photons on a FIR Camera (microbolometer, 16bit, 8-14um)
Measuring and comparing Transition, Cherenkov and Cherenkov Diffraction radiation

## Slide 36: 2. Silicon ChDR on CLEAR at CERN
In-air spectral-angular measurement of ChDR in an half silicon wafer radiator.
Detector: PDA10 InGaAs (0.9-2.6um) single pixel photodiode mounted on a motorized Goniometer.
Set of bandpass filters used to select wavelength (BW 30nm).
Si Radiator
e- Beam
ChDR

## Slide 37: 2. Silicon ChDR on CLEAR at CERN
Installation on going in CALIFES

## Slide 38: Cherenkov radiation (1/2)
‘Equivalent to the supersonic boom but for photons’
Threshold process: Particles go faster than light b > 1/n
n is the index of refraction
b is the relative particle velocity
qc is the Cherenkov light emission angle
d the length of the cherenkov radiator
The total number of photons proportional to the thickness of the Cherenkov radiator
Almost no dependency on beam energy

## Slide 39: Cherenkov radiation (2/2)
Emitted (measurable) power spectrum depends on the materiel transparency (Tr(l))
CVD SiC
Silicon
SiO2
Diamond
Al2O3

## Slide 40: …Using beam parameters of LHC

## Slide 41: e.g. Positioning of Crystal collimator in LHC or FCC

## Slide 42: e.g. Positioning of Crystal collimator in LHC or FCC
LHC collimators are equipped with electrostatic BPM to allow their alignment with a resolution better than 10microns in10-20seconds at a distance of few mm from the beam
42
LHC collimator aperture
(≈1mm) at 7TeV
Equipped with BPM button
on both end of the jaw (1m long)

## Slide 43: e.g. Positioning of Crystal collimator in LHC or FCC
43
Crystal collimators are now seriously considered as the future primary collimators in LHC and FCC
  Investigating the use of Cherenkov Diffraction Radiation as way to measure the position of the crystal with respect to the beam
LHC collimators are equipped with electrostatic BPM to allow their alignment with a resolution better than 10microns in10-20seconds at a distance of few mm from the beam

## Slide 44: e.g. Cherenkov Diffraction Radiation
Wavelength (m)
h=1mm
h=2mm
h=3mm
Photon
Spectrum (a.u)
Peaking @1-3um
ChDR Photons spectrum in Silicon for LHC (7TeV protons) and different impact parameters
Silicon – n=3.45
Photon spectrum only calculated over the transmission bandwidth of
corresponding material

## Slide 45: e.g. Cherenkov Diffraction Radiation
Wavelength (m)
Photon
Spectrum (a.u)
Better to Detect
in the FIR
450GeV
7TeV
50TeV
Number of ChDR photons and ChDR power spectrum as function of beam Energy (LHC-FCC)
  1m Si crystal and impact parameter h = 2mm
Proton Beam Energy (MeV)
Nph
per proton
LHC 450GeV
LHC 7TeV
FCC
Nph=300
Nph=11500
Nph=39000

## Slide 46: e.g. Positioning of Crystal collimator in LHC or FCC
Impact parameter (m)
Photon Power (W)
3mm long Silicon Crystal and 7TeV protons
Emitted Photon power for h=1mm (typical for primary collimators) ≈ 5watts for full LHC beam
2808 nominal bunches (1.1E11 protons)
Wavelength
[1-20um]

## Slide 47: e.g. Positioning of Crystal collimator in LHC or FCC
Impact parameter (m)
Photon Power (W)
qc=73.1°
p/2 - qc < qTotR
qTotR
3mm long Silicon Crystal and 7TeV protons
Emitted Photon power for h=1mm (typical for primary collimators) ≈ 5watts for full LHC beam
2808 nominal bunches (1.1E11 protons)
In current design (i.e. parallel crystal faces), a large fraction of the power would be totally reflected (16,9°) and possibly absorbed
  Crystal outer face built with different angle or with a high roughness to diffusive the light out
  Measuring infrared photons coupled in a optical fiber

## Slide 48: ChDR for Beam cooling ?

## Slide 49: ChDR for Beam cooling ?
During normal operation, LHC luminosity drops over a fill due to beam losses
Synchrotron Radiation cooling time is 21hours
  Particle energy lost by SR is approximately 7keV per turn (80MeV.s-1) with a critical energy at 42eV
  Effect of SR Transverse beam cooling is not visible on the peak luminosity

## Slide 50: ChDR for Beam cooling ?
Cool the beam transversely in 4-5 hours to maintain the peak luminosity constant : Gain in integrated luminosity

## Slide 51: ChDR for Beam cooling ?
Assuming a ring shaped radiator, the energy lost by one proton in a 1m long Diamond radiator as function of impact parameter h
To be compared to 7keV energy lost per turn by SR
Energy lost
per turn (eV)
Impact parameter h (m)
CVD Diamond

## Slide 52: ChDR for Beam cooling ?
Acceleration
Acceleration
Turn 1 ------------------------------------------> Turn n
It requires that Particle recoils opposite to its direction of propagation
Assuming this is true (or partially true), the emittance of the beam would then decrease down to an equilibirum emittance – What would that be ?
Assumed that radiator is thin enough so that there is no coherent emission
Radiating and Cooling

## Slide 53: ChDR for Beam cooling ?
Emittance
reduction De
Time (h)
Time evolution of the LHC beam emittance at 7TeV for different impact parameter h
h=1mm
h=1.5mm
h=2mm
Assuming 10x 1m long Diamond radiators

## Slide 54: ChDR for Beam cooling ?
Damping time (h)
Beam energy (MeV)
LHC@450GeV (weeks)
LHC@7TeV
(≈5hours)
FCC (minutes)
Damping time as function of beam energy (h=1.5mm)
Damping time = the time it would take particle to lose half of its energy
Assuming 10x 1m long Diamond radiators

## Slide 55: ChDR as source of Radiation ?
T. Lefevre, 7th Channeling Conference, Sirmione, 2016

## Slide 56: ChDR as source of Radiation ?
Beam energy | 3 GeV
Beam current | 200mA
Ring Circonference | 220m
bending magnet photon flux

## Slide 57: ChDR as source of Radiation ?
Wavelength (m)
Flux (photons/s/0.1%BW)
h=1mm
h=2mm
h=3mm
ChDR from a 1cm long
diamond radiator
Beam energy | 3 GeV
Beam current | 200mA
Ring Circonference | 220m
bending magnet photon flux

## Slide 58: ChDR as source of Radiation ?
1cm long
diamond
Wavelength (m)
Flux (photons/s/0.1%BW)
h=1mm
h=2mm
h=3mm
Several orders of magnitude difference
≈107-108
Beware, this is the ChDR photon flux produced and not extracted (x10-3) !
If interested in longer wavelength (FIR/THz) – use larger impact parameter
bending magnet photon flux

## Slide 59
Experiment installed at ATF2 in February 2016, in the laser-wire previous location where vertical beam can be focused to < 1um
ODRI experiment at KEK ATF2
Notes: Installation in Feb 2016

## Slide 60
ODRI experiment at ATF2
The target as 4 slits for DR (50 to 201 µm)
A couple of vertical and horizontal mask slits can be inserted 13 cm upstream the target
ODR
Masks
TARGET
e- Beam
Synchronous Imaging and Angular acquisition for position filtering in angular

## Slide 61
ODRI at ATF2
Direct Image of the ODRI
2D Angular distribution of the ODRI