## Slide 1
Particle Accelerators
Ubaldo Iriso
Accelerator Division
ALBA Synchrotron
(focusing on sync. light sources and ALBA)

## Slide 2
…machine that uses electromagnetic fields to propel charged particles to very high speeds and energies, and contain them in well-defined beams.
…variety of accelerators…
What is a Particle Accelerator?

## Slide 3
~30000 accelerators worldwide
Types of Accelerators
Notes: The introduction of dopants in a semiconductor is the most common application of ion implantation.
Ion implantation is one of the fundamental processes used to make microchips. Raw silicon is neither a perfect insulator nor a perfect conductor. It’s somewhere in the middle. Inserting a smattering of boron or phosphorus atoms into the silicon crystal lattice allows us to control the flow of electricity through the silicon and make transistors – the building block from which we make chips

## Slide 4
1. Ion implantation
Modify material properties for industrial applications
Radio-isòtops
Circumference ~1m
IBA (Bèlgica)
Ion implantaion
~10m lenght
HZB (Alemanya)
2. Medical applications
Radio-therapy: Cancer/tumor treatments
Types of Accelerators

## Slide 5
3. Particle Colliders: Particle and Nuclear Physics
Types of Accelerators
Colliders are actually TWO accelerators:
Two particle beams rotate in opposite directions
They cross at certain “collision points”, where massive detectors try to take a picture of the collision sub-products:
Particle discovery, quark-gluon plasma states…
RHIC Lay-out
New York (USA)

## Slide 6
Large Hadron Collider - LHC
Circumference ~27km
Ginebra (Suïssa / França)
3. Particle Colliders: Particle and Nuclear Physics
Types of Accelerators

## Slide 7
Name | Location | Circumf. | Particle | Energy
RHIC | New York (USA) | 3.8km | p / Au+ | 0.250 GeV
Tevatron | Chicago (USA) | 6.3km | p | 1 TeV
KEK | Tsukuba (Japó) | 1.5km | e- / e+ | 12 GeV
DESY | Hamburg (Alemanya) | 6.4km | e- / p | 27 GeV / 938 GeV
LHC | Ginebra (Suïssa) | 27km | p – p (Pb+) | 7 TeV
3. Particle Colliders: Particle and Nuclear Physics
Types of Accelerators

## Slide 8
Types of Accelerator: future...
LHC
FCC
FCC (2035) – C ~[80 – 100] km, E=100 TeV

## Slide 9
ALBA Synchrotron
Circumference 270m
Cerdanyola (Barcelona)
Types of Accelerators
4. Synchrotron Light Sources:
“see” material structures in molecular/atomic scales
interdisciplinar applications: biology, chemistry, nanotechnology…

## Slide 10
Types of Accelerators
4. Synchrotron Light Sources:
“see” material structures in molecular/atomic scales
interdisciplinar applications: biology, chemistry, nanotechnology…
Around 60 synchrotron light source in operation
(or construction)

## Slide 11
Particle Acceleration:
electric fields

## Slide 12
“Stripping” H atoms
Particle’s Origin: protons

## Slide 13
Particle’s Origin: electrons
Thermo-electric effect:
Heat metal to temperature ~1000ºC until electrons are released
High voltage to extract the electrons (90kV at ALBA)

## Slide 14
First Accelerators: LINACs
LINAC, LBL, 1957
First Linacs (Wideroe, ~1930):
- e-gun followed by drift tubes with electrostatic potential between them
- Idea and first prototypes in the 1930s: drift tubes suspended in a non-conducting tubes.
Drift Tube Linacs (Alvarez, ~1950):
- Drift Tube Linacs (DTL) use conducting waveguides, which is still the typical structures of actual LINACS
e-Gun

## Slide 15
First Accelerators: LINACs
ALBA Linac (12 m):
  -first of ALBA Accelerator complex
  -creates e- and accelerates them from 90kV to 100MeV

## Slide 16
DC electric fields are limited to ~1MV/m due to dielectric breakdown
Instead, AC electric fields are used to reach high electric fields (~10MV/m)
These fields are produced in the so-called “radio-frequency ressonant cavities” , or just rf cavities
Particle Acceleration: rf systems
At ALBA:
E ≈ 10 MV/m @ 500 MHz
Notes: A més, accelerar amb voltatges electrostàtics (DC) està limitat a V~1MV/m degut a la ruptura dielèctrica de l’aire

## Slide 17
But passage of particles needs to be synchronized with the sinusoidal rf field in the cavities
The beam cannot be a continuous of particles, but travel in “bunches”:
  Bunch spacing = rf wavelength
  ALBA: f=500 MHz  lrf=60cm
lrf
Particle Acceleration: rf systems

## Slide 18
Particle Acceleration: rf systems
So the bem orbit length “L” has to fulfill:
L = lrf ·h
  with h = Integer number (hALBA =448)
Since electrons travel at light speed:
lrf = c / frf  frf = c·h / L
 tracking freq rf (frf) allows to track changes in the orbit length of the accelerator (L)
Rf cavity
In circular accelerators, bunches need to pass again by the cavity in synchronism with the electric field:

## Slide 19
Particle Acceleration: rf systems
RF Frequency and Orbit Length (i.e. circumference)
frf = 499.644MHz +- 20Hz
Precision ~1e-7
Peak-to-peak orbit amplitude:
+/- 27um.
After the first 6 years o operation, the average RF frequency decreased by 3.1kHz, corresponding to an increase of the electron beam path of +1.7mm
DL (2012 – 2018) = 1.7mm

## Slide 20
Particle Acceleration
ALBA RF Cavity
DAMPY Cavity:
european collaboration among several synchrotrons to avoid high order resonances
Precise design to control shape, constant monitoring of temperature…
Everything influences the cavity resonant frequency (so, the orbit lenght!)

## Slide 21
Particle Guidance:
magnetic fields

## Slide 22
Particle Guidance: magnetic fields
Motion control is purely done with magnetic fields using the Lorentz Force
Magnetic field perpendicular to the electron velocity produces a transversal force and change trajectory

## Slide 23
Two coils with high current produce constant magnetic field between two poles (N/S)
By applying the Lorentz Force, particles bend and change their trajectory
N
S
Magnetic field at fridges: B~20 Gauss
Magnetic field at ALBA dipoles: B~14 000 Gauss
Electrical Current at coils: 600 A
Particle Curvature: dipolar magnets
Particle Guidance: magnetic fields

## Slide 24
Particle Guidance: magnetic fields
Particles with different energies get dispersed transversely in space
Need something to group them again
 Quadrupole magnets
Particle Curvature: dipolar magnets
But the energy of the beam is not a Dirac delta distribution, but has a Gaussian distribution DE~0.1%

## Slide 25
Particle Guidance: magnetic fields
Particle Focusing: quadrupolar magnets
Note: focus on hor plane  defocus on ver plane
Quadrupoles usually go in pairs or triplets

## Slide 26
Particle Guidance: magnetic fields
Particle Focusing: quadrupolar magnets
But the energy of the beam is not a Dirac delta distribution, but has a Gaussian distribution DE~0.1%
Particles with different energies focused at different long locations
Need something to group them again
 Sextupole magnets

## Slide 27
Particle Guidance: magnetic fields
Correct Chromatic effects: sextupole Magnets

## Slide 28
Synchrotron Radiation

## Slide 29
Synchrotron Radiation
Synchr. light
Relativistic charged particles emet synchrotron radiation when they are bent in a dipole
The spectrum of this synchrotron radiation goes from near infrared to hard x-rays
General Electrics (1947)
N
S

## Slide 30
beamline
beamline
First experiments with synchrotron light were “parasitic” experiments from particle colliders
They just use the radiation produced by dipoles when the particles were bent
Experiments were done in the experimental beamlines
Synchrotron Radiation

## Slide 31
Wisconsin (USA), 1968 – 1987
C = 9m (octogonal shape!)
E=240 MeV
8 dipoles + 4 quads + 1 rf cavity
Two dipoles were used to extract synchrotron light
Tantalus: first accelerator designed purely to produce synchrotron light
RF
dipols
Synchrotron Radiation

## Slide 32
Wisconsin (USA), 1968 – 1987
C = 9m (octogonal shape!)
E=240 MeV
8 dipoles + 4 quads + 1 rf cavity
Two dipoles were used to extract synchrotron light
Tantalus: first accelerator designed purely to produce synchrotron light
Synchrotron Radiation

## Slide 33
injecció
After Tantalus, the scientific community started to exploit the synchrotron radiation
In the early 90s, the so-called “3rd Generation of SLS” were designed such that:
Maximize synchrotron light flux
Allow experiments in most stable conditions
Maximize space for Insertion Devices
beamline
beamline
Synchrotron Light Sources (SLS)

## Slide 34
Synchrotron Light
Small dipole arrangements
Electrons are forced to bend, producing strong emission of synchrotron radiation
Types of IDs:
  Unduladors: coherent light
  Wigglers: incoherent
Insertion Devices
(see D. Heines presentation)

## Slide 35
Accelerator Lattice

## Slide 36
Accelerator Lattice
Magnets (dipoles, quadruples, sextupoles) are placed around circular accelerator in a periodic arrangement called “lattice”.
ALBA Lattice: 16 symmetrical cells
Synchrotron Light Sources: lattice design should leave space for Insertion Devices
¼ of the ALBA Ring
Cell - 1
Cell - 2
Cell - 3
Cell - 4

## Slide 37
Accelerator Lattice
Particle Tracking ¼ of the ALBA ring

## Slide 38
Particle Tracking ¼ of the ALBA ring
Accelerator Lattice

## Slide 39
Particle Tracking ¼ of the ALBA ring
Accelerator Lattice

## Slide 40
Particle Tracking ¼ of the ALBA ring
Accelerator Lattice

## Slide 41
Particle Tracking around the ALBA ring
At each point of the accelerator circumference “s”, the distribution of position and angle (x, x’) describe and ellipse:
The shape of the ellipse changes with s, but the area is constant: e is invariant.
This is what we call “emittance” , and it is the figure of merit of a synchrotron light source
Accelerator Lattice

## Slide 42
Particle Tracking around the ALBA ring
Accelerator Lattice

## Slide 43
Particle Tracking around the ALBA ring
Accelerator Lattice

## Slide 44
Particle Tracking around the ALBA ring
Accelerator Lattice

## Slide 45
Accelerator Lattice: emittance
Synchrotron Light Sources are optimized to maximize photon flux.
This is computed by the Brilliance, or spectral brightness:
This can also be expressed as a function of the emittance:
The smaller the emittance the highest the brlliance

## Slide 46
ALBA Upgrade

## Slide 47
LINAC:
100 MeV
BOOSTER:
100 MeV – 3 GeV
STORAGE RING:
100 MeV – 3 GeV
ALBA Upgrade
ALBA Accelerator Complex Today

## Slide 48
LINAC:
100 MeV
BOOSTER:
100 MeV – 3 GeV
STORAGE RING:
3 GeV
ALBA Upgrade
Only change is the magnet lattice
The rest is kept: including beamlines
ALBA Accelerator Complex 2031(?):

## Slide 49
Take profit of the latest magnet technology progress
New design of the lattice to keep emittance around 20 times smaller
ALBA Upgrade
ALBA
ALBA-II

## Slide 50
 | Size (σ) | Divergence (σ’)
Horizontal | 132 µm | 48.5 µrad
Vertical | 7.7 µm | 5.9 µrad
ALBA
e=4.6nm·rad
 | Size (σ) | Divergence (σ’)
Horizontal | 15 µm | 10 µrad
Vertical | 5 µm | 3.16 µrad
ALBA-II
e=0.160 nm·rad
ALBA vs ALBA-II: the electron beam

## Slide 51
ALBA Upgrade
Notes: suposaria una millora en les prestacions de les beamlines: experiments més ràpids, menys soroll al detectors…
More coherence , so different experiments, better resolution

## Slide 52
ALBA Upgrade

## Slide 53
ALBA Upgrade
2019: preliminar lattice design
07/2021: approval of ALBA-01, project to build magnets prototypes
2022: write CDR
2024 – 2028: Design and construction

## Slide 54
2029 – 2030: black period to exchange magnets
2031: start of ALBA-II
ALBA Upgrade
2019: preliminar lattice design
07/2021: approval of ALBA-01, project to build magnets prototypes
2022: write CDR
2024 – 2028: Design and construction
(if finally approved)

## Slide 55
Gràcies!

## Slide 57
Acceleradors de Partícules
https://public.cells.es/machine-status/msGUI.html

## Slide 58: Questions welcome