## Slide 1: Sincrotrón ALBA: Proyecto ALBA II
AEC2 Visit – Dec 17th, 2024

## Slide 2: ALBA is the Spanish Synchrotron Radiation Facility
National Public institution with funding 50%/50% from the Spanish Ministerio de Ciencia e Innovacion and the Catalan Department de Recerca i Universitats
National and international (28%) staff
National and international (40%) users
National and international collaborations
The ALBA Team
We are today ≈250

## Slide 3
ALBA key parameters
JEMCA
Joint Electron Microscope Center at ALBA
50% Funded through Catalan ERDF, and
50% co-funded by different partners
e- Energy = 3 GeV
C = 270 m
Emittance = 4.4 nmrad
11 operating BLs
2 in commissioning
1 in construction
2 for acc. diagnostics
2500 User visits
3500 Publications

## Slide 4
Evolution of ALBA to the 4th Generation ALBA II
ALBA II upgrade Project
Design & construction
Exploitation
Design & construction
Exploitation
2003 2012 2022 2031 2050
3rd Generation
4th Generation

## Slide 5: ALBA II upgrade Project
The upgrade ALBA II includes:
renovation of the storage ring
renovation of the existing beamlines.
expansion of the infrastructure.
construction of up to three new long beamlines.
synergy to create a scientific and technological pole in the area.
The adjacent land is already
secured for ALBA II

## Slide 6: ALBA II Accelerator Upgrade
Upgrade the 3rd Generation ALBA Storage Ring
to a 4th Generation Ultra Low Emmittance Ring: ALBA II
with the aim of doing it as efficiently as posible,
in terms of cost and time.
ALBA II
ph/s/mrad2@0.1%BW
Simulation of the flux density emitted by IVU21 (XALOC)
2.5E17
ALBA
ph/s/mrad2@0.1%BW
0.5E17

## Slide 7: Accelerator’s design constrains
Keep beam energy 3 GeV
Keep the tunnel  SR with similar compact circumference
Keep existing ID beamlines  preserve 16 cells and source points
Bending beamlines can be relocated
Keep injector (present εxbooster = 10 nm∙rad)
Keep infrastructures, as much as possible
Straight sections 4 m, with βx βy 2 m
Reduce emittance by more than a factor 10 (<400pmrad)

## Slide 8: Accelerator’s upgrade
 | ALBA
Energy | 3 GeV
Circumference | 268.8 m
Symmetry | 4-fold
Lattice | 8×2 DBA cells
Emittance | 4.5 nm·rad
Nº of cells | 8+8
# of straights | 4 / 12 /8
Straight length | 7.8 / 4.0 / 2.3m
ALBA II
3 GeV
268.8 m
4-fold
16×MBA cells
~200 pm·rad
16
16
4.0 m
0
matching cell
unit cell

## Slide 9: Prototypes
A series of prototypes are being produced to test the main components:
MAGNETS
VACUUM CHAMBERS
+ Permanent magnets version
Absorber
Vacuum chambers

## Slide 10: Prototypes
A serie of prototypes are being produced to test the main components:
GIRDERS
BPMs
Yaw
Y, X
Buttons BPMs

## Slide 11: Prototypes
A serie of prototypes are being produced to test the main components:
PULSED Doble Dipole Kicker
3rd Harmonic Active RF system
Being tested at BESSY II Bunch lengthening of single bunch
Field profile for single kicker injection

## Slide 12: ALBA II implementation (2030-31)

## Slide 13
Accelerator’s components
2026-2029
New magnets
  ∼ 600 electro-magnets
  ∼ 1000 power supplies
  ∼ 40 permanent magnets
New vacuum chambers
  ∼ 270 m vacuum chambers
  SS, Cu, NEG coated
New Girders
  High vibration modes
  High precision remote movement
Many others:
  Upgrade RF system with SSA and 3rd Harmonic Cavity
  New Diagnostics equipment
  New Insertion Devices
  Upgrade electronics
  …