## Slide 1: The beamlines of ALBA II
Josep Nicolas

## Slide 2
ALBA II beamline program
Spectroscopy (external atomic levels, core levels of light elements)
Spectroscopy
(Core level)
Diffraction
Imaging + Tomography
Imaging + Tomography
UV
soft x-rays
hard x-rays
Spectroscopy
Diffraction
Tomography
To measure absorption (or photoemission, ionization, fluorescence, etc.) as a function of photon energy.
It gives information of the internal structure of electrons inside the atoms, and how they change during processes.
To measure the diffraction pattern of x-rays after crossing a sample.
Allows reconstructing the structure (geometry) in which atoms are laid out in a solid)
Take images (with or without focusing) of the sample from several perspectives and reconstruct its 3D volume.
New!
New!
New!
New!

## Slide 3
BL02-CODI
BL03
Main building
Far Experimental Hall
Stream course
(not usable)
BL-04 CORUS
BL08
BL07-Calima
BL15-3sbar
Notos
3sbar
Claess
Circe
Minerva
Boreas
Faxtor
Miras
Xaira
Mistral
NCD-sweet
Xaloc
MSPD 2
A) Construction of 4 new beamlines
B) Upgrade of the 13 existing beamlines of ALBA
ALBA II beamline program

## Slide 4
Soft x-ray spectro-microscopy (BL24-CIRCE)
Spectroscopy (combined with microscopy) allows imaging the atomic layers as they grow in a crystal, allowing understanding the processes at a fundamental level
We can also ‘image’ the magnetic domains, and study how small they can be and still b stable, and how fast we can change them.

## Slide 5
G
NM
n
N: nucleus
NM: nuclear membrane
ER: endoplasmic reticulum
G: golgi
n: nucleoli
M: mitochondrion
LV: lipid vesicle
N
NM
M
M
M
ER
LV
Soft x-ray micro-tomography (Mistral)

## Slide 6
X-ray diffraction (MX)
From the diffraction pattern we RECONSTRUCT the 3D STRUCTURE of the protein (or any large molecule)
Xrays

## Slide 7
X-ray diffraction (Powder Diffraction)
Powder diffraction allows studying the changes in the atomic structure while the sample is interacting with something. In this case, as a battery material is charged and discharged.
X-rays

## Slide 8
Beam Size
310 x 18 µm2 fwhm
45 x 27 µm2 fwhm
ALBA
ALBA II
The ALBA II as a light source
Brilliance is the flux of photons emitted
from the same point (Δx) (smaller)
in the same direction (Δα). (more collimated)
Δx Δα ≥ λ/2π
x4
ALBA
ALBA II
x8
x12
The electron-beam will be
smaller
less divergent
Therefore more intense (more brilliant)
Wavelength is the limit on how much we can reduce the size and divergence of the source.
Near this limit, light behaves more as a wave and less as a geometric ray.
It shows diffraction and Interference effects (we say light is is coherent) .
Difraction limit

## Slide 9
Brightness / coherence
Superbends
More flux on diffraction beamlines.
Wave optics for x-rays.
Approach ultimate resolution limit.
Diffraction and imaging
Better spatial resolution at large working distance.
Coherence at high photon energy.
Nanoprobes and imaging
40 m BL
230 m BL
Long beamlines
Enable the use of BM beamlines for higher photon energies.
Spectroscopy and diffraction
x20
Low coherence
High coherence
The features of ALBA 2

## Slide 10
ALBA-II
Low Emittance
Super-BM
Coherence (mainly SXR)
Brilliance
(mainly HXR)
More ph/s on sample
High Energy for BMs
“Wave” properties
smaller spot size
faster collection
Big-Data methods
Ptychography
Imaging
Coherent diffractions
STXM
nanoprobes
Dynamics
Hi-throughput
Higher coherence, smaller spot size and higher photon flux density drive the development of usual and new experimental techniques.
Beamlines need to include new technologies to enable such development.
IDs
Optics
Optics
Data infr.
Stability
Accuracy
Fast scan
Fast scan
Fast detectors
Only a few examples of enabling technologies are indicated
New generation Optics
New generation Mechanics
Controls technology
Data handling
Benefits for photon science

## Slide 11
BL02-CODI
BL03
Main building
Far Experimental Hall
Stream course
(not usable)
BL-04 CORUS
BL08
BL07-Calima
BL15-3sbar
Notos
3sbar
Claess
Circe
Minerva
Boreas
Faxtor
Miras
Xaira
Mistral
NCD-sweet
Xaloc
MSPD 2
A) Construction of 4 new beamlines
B) Upgrade of the 13 existing beamlines of ALBA
ALBA II beamline program

## Slide 12
M1 (mcyl)
M2 (scyl)
Top view
HFM
HXS
VFM
DCM
VXS
IVU19
Sample
Tunel
Exp. Hall
Far Exp. Hall
17.541
42.560
134
249
19.5
19.8
40.0
40.3
230
230.4
230.17
2.5 mrad
2.5 mrad
3.2 mrad
SLIT2
Side view
5.5 mrad
Source
Focusing optics and monochromator
Secondary source
Refocusing optics and end-station
BL02-CoDi Optical layout

## Slide 13
80
40
120
165
VFM
HFM
80
202.5
122.5
Plano-elliptic mirrors
Graded multilayer coating
Rmin ~ 10 m
Length >80 mm
Figure Errors < 1 nm, < 50 nrad
Transversal acceptance < 1 mm2
The intended nanoprobes represent a challenge, first in optics
Spot size <25 nm fwhm
Depth of focus < 10 µm
Distance to sample <40 mm
Nanofocusing optics

## Slide 14
Nanoprobes
Long beamlines allow achieving this with sufficient space around the sample to set a “sample environment
Sample
Detector(s)
Optics
Reactive Gases
Electr.Field
Heat
Laser
Cryogenics
Strain
A nanoprobe allows obtaining spectra or diffraction data with spatial resolution over the sample.
It produces “images” in which each pixel is a complete spectrum or a complete diffractogram.
Its spatial resolution is given by the size of the focused beam (ca. 30x30 nm for ALBA II)

## Slide 15
 | CoDI
Source | In vacuum undulator (IVU19)
Energy Range | 10 - 30 keV (DCM + MLM)
Spot Size | 30-50 nm
Technique | nanoDiffraction, nanoFluorescence, CDI, Ptychography, Holography, Bragg-ptychography, Tele-ptychography
Features | 20 m flight tube Laser Heating, High Pressure, Gas dosing, Cryostream, Cryostat… (space around sample for versatile sample environment)
Sample | Micro reactors / Electro chemistry cells for in-situ and operando
Detector | One large area detector (6M type) One small detector mounted on robot arm Multielement SDD
Hard X-ray nanoprobe beamline devoted to Coherent Diffraction Imaging techniques, for in-operando studies in material science.
3D reconstruction and Evolution of strain in a Pt nanoparticle as varying electrode potential. Useful for the design of strain-engineered nano-catalysts
From C. Atlan, et al. Nat. Mater. 23, (2023). https://doi.org/10.1038/s41563-023-01528-x
BL02-CoDi

## Slide 16
 | Corus
Source | In vacuum undulator (IVU19)
Energy Range | 10 - 27 keV (DCM + MLM)
Spot Size | 20-50 nm
Technique | 3D-nanoXRF, XANES (STXM) Holo-tomography (Full Field)
Features | LN2 cryogenics, 180º Rotation, XY mapping UHV, Visible microscope
Sample | Multi-sample shuttle system
Detector | Nanospec:: Two Multielement SDD, Diode NanoImag: Two Multielement SDD, sCMOS Area detector.
Determination of intra-cellular location of Ir in breast cancer cells. Imaging at nm-resolution with chemical sensitivity.
Hard X-ray nanoprobe beamline devoted to spectral Imaging and tomography for life sciences.
From Conesa et al. Angew Chem Int Ed Engl 2020, 59 (3), 1270-1278. DOI:10.1002/anie.201911510.
BL04-Corus

## Slide 17
ALBA
ALBA-2
ALBA-2
+Superpolished mirrors
ALBA-2
+Superpolished mirrors
+Adaptive Optics
1
x14
x36
x48
 | AXO | Super Polished | Flux | Fluxdens | Size | Brilliance | Brilliance factor
ALBA |  |  | 4.5E+12 | 9.8E+11 | 2.9x1.4 | 2.3E+19 | 1
ALBA-2 |  |  | 1.5E+13 | 8.3E+12 | 0.8x1.1 | 3.3E+20 | 14
ALBA-2 |  | YES | 1.5E+13 | 2.1E+13 | 0.4x0.7 | 8.4E+20 | 36
ALBA-2 | YES | YES | 1.6E+13 | 2.7E+13 | 0.6x0.7 | 1.1E+21 | 48
Simulations of the beam on sample for XAIRA, assuming perfect alignment and stability
Impact of BL upgrades

## Slide 18
Sample
Sample
Detector
Detector
Optics
Low brilliance: photon flux is distributed in a large/collimated or small/diverging beam
High brilliance: The same photon flux is are distributed in a small and collimated
Optics
More beam accepted.
Lower aberrations
Smaller spot
Higher flux density ( ~40 times)
More collimated
More intense
Smaller spot in detector (= Higher coherence distance on sample)
The benefits of brilliance
Source
Source

## Slide 19: Thank you
jnicolas@cells.es