## Slide 1: MAINTENANCE from the CONTROL ROOM Montse Pont

## Slide 2: Outline
Introduction to ALBA accelerators
ALBA operation & performance
Maintenance
Summary

## Slide 3
BOOSTER
100 MeV ->
3 GeV
LINAC
100 MeV
STORAGE RING
3 GeV
Parameter | Value
Energy | 3 GeV
Circumference | 268.8 m
Emittance | 4.5 nm·rad
Current | 250 mA
RF frequency | 500 MHz
# cavities | 6
Long straights | 4 (8 m)
Medium straights | 12 (4 m)
Accelerators layout

## Slide 4
100 MeV LINAC
LINAC @ 100 MeV
Charge: 1 nC
Rep rate 3.125 Hz
Flexible e-gun: flexible filling patterns
Linac

## Slide 5
Extraction
BOOSTER
Booster
Parameter | Value
Nominal inj E | 100 MeV
Minimum inj E | 60 MeV
Nominal ext E | 3 GeV
Circumference | 249.6 m
Emittance | 10 nm·rad
Nominal Current | 1 mA
Rf frequency | 500 MHz
# cavities | 1
In the same tunnel as the SR | 

## Slide 6
STORAGE RING
Parameter | Value
Energy | 3 GeV
Circumference | 269.9 m
Emittance | 4.5 nm·rad
Nominal Current | 250 mA
Rf frequency | 500 MHz
# cavities | 6
Long straights | 4 (8 m)
Medium straights | 12 (4 m)
Short straights | 8 (2 m)
Storage Ring

## Slide 7
BO and SR share the same tunnel
Normal conducting magnets & cavities
2xIVU, 1xMPW, 1xSCW, 2xAPPLE-II, (1xAPPLE-II, 1xIVU, 1 x MPW)
BO & SR

## Slide 8
Bending: e- Diagnostics
BL04: MSPD
SCW31 – (8-50 keV)
HP/HR
Powder Diffraction
BL09: MISTRAL
Bending– (0.27-2.6 keV)
X ray Microscopy
BL11: NCD
IVU21– (6-13 keV)
Non Cristalline Diffraction
SAXS/WAXS
BL13: XALOC
IVU21 – (5-22 keV)
Macromolecular Cristallography
BL22: CLÆSS
MPW80– (2-63 keV)
Absorption &
Emission Spectroscopies
BL24: CIRCE
EU62– (0.1-2 keV)
Photoemission
spectroscopies
BL29: BOREAS
EU71– (0.08-3 keV)
Resonant Absorption
and Scattering
BL01: MIRAS
Bending – (0.4-100 µm)
IR Spectroscopy
BL20: LOREA
EU125 – (10-450 eV)
ARPES
In operation (8)
In construction (4)
BL06: XAIRA
IVUXX (~5-25 keV)
Macromolecular Cristallography
BL16: NOTOS
Bending
Metrology, XAS
BLXX: FaxTor
ID: 3 pole wiggler
Hard x-ray tomography
Beamlines

## Slide 9: Operation & Performance

## Slide 10
Beam current since 2012
Inom

## Slide 11
Top-up operation since 2014
Re-injection every 20 min (DI = 2.0 %)
Injection efficiency around 90%
Gating to blank injections is available. IR BL uses it
Top-up operation

## Slide 12
Filling pattern
Usual 8-10 (MBM) trains
For BL24_PEEM
MBM + n x SB
Michael Foerster et al. Nature Communications (2017)
Hybrid with 1 SB
LINAC MBM pulse
LINAC SB pulse

## Slide 13
100Hz
Ver:
100 nm
Hor:
600 nm
Well below specs of 10% of beam size
600 nm < 1% of σX at ID (132 um)
100 nm < 1.5 % of σY at ID (7.5 um)
Orbit stability
Integrated amplitude [nm]
Frequency [Hz]

## Slide 14
Vertical beam size
Coupling control using skew quadrupoles
Coupling of 0.11%
sy = 15 um
ey = 5 pm·rad
Coupling of 0.59%
sy = 28 um
ey = 28 pm·rad

## Slide 15
Operational performance
24/7
8 Runs
4 - 5 weeks / Run
5888 h Total (80% for BLs)

## Slide 16
Chart: 
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Total op hours | 3280 | 4464 | 5250 | 5730 | 5760 | 5888 | 5912
Scheduled user beam [h] | 2387.3 | 3539.5 | 3740 | 4320 | 4365 | 4632 | 4680
Machine development | 892.7 | 924.5 | 1510 | 1410 | 1395 | 1256 | 1232
Operational performance
6000 h of operation:
consolidated

## Slide 17
until 24/09/2018 BA: 98.0%
MTBF: 104 h
MTTR: 2.1 h
Operational performance
Chart: Beam availability [%]
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
BA | 77 | 83.8 | 96.8 | 97.3 | 97.6 | 98.3 | 98
MTBF | 21 | 25 | 33.7 | 51 | 58.2 | 99.7903 | 104

## Slide 18
Operational performance
Down time analysis in 2017
  Systematic analysis of all events
  Including events not generating a beam dump

## Slide 19
First fixed, patch, repair, and re-inject (“happy users”)
Then look for the root cause and fix it for the future
Operators and Floor coordinators ensure smooth operation
Readiness of tools for analysis: PM, FA, …
Importance of reducing MTTR:
    Keep adequate # spares.
    Spares well marked/located/ready
    Ensure training of operators and on-call staff
    Design for redundancy, modularity
    Deal with obsolescence
Operational performance

## Slide 20: Maintenance from the CR

## Slide 21
Beam for Users
Accelerator Development and Maintenance
Shutdown - Basic systems OFF
Shutdown - Basic systems ON
5888 hours of operation
Maintenance

## Slide 22
Accelerator Development and Maintenance 1 d/week
Shutdown - Basic systems OFF 2 long shut downs
Shutdown - Basic systems ON 5 shut downs 1 w long
5888 hours of operation
Maintenance

## Slide 23
1 day/week is machine day
5 short shut downs
2 long shut downs
Organised on a week by week
Web based CTAR (request for interventions) prepared/approved
Operator in CR follows interventions, grants access, resolves interferences,..
Provides a window for short and urgent repairs
Modified at “extremely” short notice
Maintenance

## Slide 24
Coordination starts 1 month before
Main access restrictions discussed at the Operations Meeting
Web based CTAR (request for interventions) prepared/approved
Operator in CR follows interventions, grants access, resolves interferences ...
Schedule distributed the week before
Maintenance
1 day/week is machine day
5-6 short shut downs
2 long shut downs

## Slide 25
Coordination starts 3-4 months in advance through the Operations Meeting
Yearly maintenance of infrastructure
New installations/major interventions
No OP in control room. Machine is completely OFF
New in 2018: Controlled switch OFF/ON of all accelerator hardware
Maintenance
1 day/week is machine day
5 short shut downs
2 long shut downs

## Slide 26
Technical groups belong to different divisions/sections
No central maintenance programme
Missing general overview
Maintenance
Division
Sections

## Slide 27
Infrastructures:
Cooling,
Air conditioning
Electrical supply
Compressed air
Computing:
Power supplies,
All electronics,
Controls
Accelerators
RF
Magnets
Pulsed elements
Diagnostics
Preventive maintenance
using standard CMMS soft
More than 7000 equipment
700 different types of equipment
Largest series is 176
Develop our own programs and tools
See contribution by J.Manotas, J.Iglesias
See contribution by T.Camps
Maintenance tools

## Slide 28
Operations Meeting: Weekly meeting to review operation and coordinate shut downs/major activities
Jira to handle service desk (service divisions). Can be used to request a maintenance task, but is not centrally managed
Web based CTAR (orders for interventions) prepared/approved
Maintenance tools

## Slide 29
Equipment and Cable database
  Allows quick identification of components ant cables
Accelerators own maintenance programs:
  Magnets, pulsed elements, RF, LINAC
Maintenance tools

## Slide 30
ALBA is operating since 2012
Achieving goal of BA = 98%
Maintenance management is not centrally organised
Maintenance is coordinated through the Operations Meeting
Developed own tools & programs to ensure adequate maintenance of accelerator equipment
Summary