## Slide 1
ALBA II Experiments Program
Josep Nicolas

## Slide 2
Motivation…
The ALBA II upgrade is a significant investment, and it must be targeted to optimize scientific output.
Currently ALBA operates 13 BL, but it can still host 13 additional beamlines, boosting its scientific production with only a small increase of operational cost.
Some beamlines are ca. 20 yr old, besides aging, in that time there has been big improvements in several technologies: Detectors, Optics, Computing, Accelerator technology.
Research also evolves, now it demands for multimodal and multi-beamtime workflows. ALBA must embrace this.

## Slide 3
New source, new oportunities
  Smaller beam and smaller divergence allow for microfocus, higher flux on sample.
  Faster collection
  Dynamics, High throughput, Diluted simples, in operando, micro-simples.
Low Emittance  High Brilliance
ALBA
ALBA II
20 x 14 µrad2 fwhm
310 x 18 µm2 fwhm
45 x 27 µm2 fwhm
cpl 50%
Super bends (high field dipoles)
  Extend the energy range of dipole sources
Parameter | ALBA | ALBA II | ALBA II sBM
Field | 1.40 T | 1.05 T | 3.20 T
Radius | 7.138 m | 9.530 m | 3.127 m
Critical Energy | 8.39 keV | 6.284 keV | 19.15 keV

## Slide 4
New source, new oportunities
VanCittert-Zernike Thm.
Higher Coherence
Max BL length @ALBA
Length of Codi/Corus
Reasonable acceptance of a KB
The smaller source, and the long distance available for beamlines open the opportunity of Coherent Imaging Techniques.
ALBA
ALBA II
Reasonable acceptance of a FZP
Incoherent Source
Coherent beam
Focusing optics
Acceptance

## Slide 5
Three types of project
BL02-CODI
BL02-CORUS
BLnn-CALIMA
MISTRAL-U1
NCD-U1
BET-NANO
RESTART
3SBAR
BET-OPT
BET-LABS
Experiments
--
--
The Experiments Program is part of the ALBA II upgrade.
It is in turn organized in 27 projects.
Three types of project:
New Beamlines.
Beamline Upgrades
Enabling Technology
Accelerators
Infrastructures
Computing and Data
Implementation
BL33-MSPD2
BLnn-TXM 2
…
ALBA II board
Technical Direction

## Slide 6
New beamlines
Corus
CoDI
3sbar
HAXPES and Surface diffraction. Commissioning end of 2026
 Yesterday’s presentation by Juan
MSPD2
Powder Diffraction and HPMD
Procurement process in progress
Calima
BioSAXS beamline, kick-off pending
CoDI
Coherent Diffraction and Nanoprobe for Material Sciences. CDR due in October.
Corus
Nanoimaging and nanoSpectroscopy for life sciences. CDR due in October.
Calima, no port assigned
MSPD2
3sbar
BM BL, to allow splitting mistral

## Slide 7
MSPD II: a new port and source
MSPD SCW is aging quickly and compromises the continuity of its operation  Replace source by IVU
MSPD occupies one of the few ports that allow for long beamlines.  Move the BL to port BL33

## Slide 8
MSPD II: a new port and source
Contracts for the procurement of ID, FE, Hutch and Infrastructure in place
CFTs Optics and Optomechanics in preparation
The BL should be installed within 2028, to allow starting early in 2029

## Slide 9
Sec. Source Slits
(microfocus mode)
Microfocus unit (CRLs)
Sample position
Sample mounting robot
WAXS
detector
SAXS
detector
Calima is a BioSAXS beamline for ALBA for low-resolution structural analysis of samples in solution. Complementary to high-resolution crystallography BLs
Calima
The project to build Calima has not yet started, and it will not be operational before the dark period.

## Slide 10
31
 | ALBA-II (superbend) | 
Standard mode (focus at detector) |  | 
Spot at sample position | 532×590 um2 175×175 urad2 | 532×590 um2 175×175 urad2
Spot at detector position | 23×58 um2 | 23×58 um2
Microfocus mode (focus on sample) |  | 
Spot at sample position | 5.3×11 um2 428×425 urad2 | 5.3×11 um2 428×425 urad2
Spot at detector position | 1.30×1.28 mm2 | 1.30×1.28 mm2
The source is a BM
ML monochromator
KB for standard focus
CRL transfocator for microfocus
Calima Optics

## Slide 11
Sample mounting robot (HT-SAXS)
Sample holders
  Capillaries (solution), gels/solid (polymer slice, tissues, pellet), liquids/gels holder, high pressure cell (pressure induce preparation of super crystals) and shear aligning cell (fibre diffraction).
  Temperature-controlled flow cell will be placed in a vacuum chamber.
  Stopped-flow cell
  Novel continuous flow cell for TR-SAXS designed in collaboration with Dr. Ros
  Other cells will also be considered: rheometer, traction cell.
HPLC system for a variety of EC and IEC columns
Laser for photo-activation
Calima Endstation features

## Slide 12
BL02-CODI
BL03
Main building
Far Experimental Hall
Stream course
(not usable)
BL04-CORUS
CoDI and Corus are both very long beamlines, hard x-ray, devoted to imaging techniques and nano-probe techniques, with enough space around the sample
Long Beamlines: CoDI + Corus

## Slide 13
Long Beamlines: CoDI + Corus
M1 (mcyl)
M2 (scyl)
Top view
HFM
HXS
VFM
Side View
DCM
VXS
IVU19
Sample
Tunel
Exp. Hall
Far Exp. Hall
17.541
42.560
134
249
19.5
19.8
40.0
40.3
230
230.4
230.17
2.5 mrad
2.5 mrad
3.2 mrad
2.8 mrad
SLIT2
MLM
A two-stage magnification optics, with a secondary source, both vertically and horizontally.
All ‘noisy’ optics, stays in the first stage. There is nothing between the XS (intermediate source) and the refocusing KBs (at the endstation)
XS clips the beam spatially, SLIT2 clips the beam angularly. This allows for optimal control of the phase-space acceptance (to control coherence)
Total reflection KBs for refocusing, optimized for different energies.
Our main concerns are.
  Flux (very long beamlines, very small acceptance)
  Stability. Different slabs, how to steer the beam.

## Slide 14
BL02-CODI
BL04-Corus
Transfer lines

## Slide 15
Corus nanoImag
80
40
120
165
VFM
HFM
80
202.5
122.5
Parameter | HFM |  |  | VFM |  | 
Energy | 10 keV | 19 keV | 27 keV | 10 keV | 19 keV | 27 keV
Length | 165 mm |  |  | 80 mm |  | 
Object distance | 233.2 m |  |  | 233.023 m |  | 
Image distance | 202.5 mm |  |  | 80 mm |  | 
Incidence angle | 1.15º | 0.90º | 0.65º | 1.15º | 0.90º | 0.65º
Coating | ML W/B4C |  |  | ML W/B4C |  | 
Period | 3.0 nm | 2.1 nm | 1.9 nm | 3.0 nm | 2.1 nm | 1.9 nm
Working dist. | 120 mm |  |  | 40 mm |  | 
Slope Error | <75 nrad rms |  |  | <75 nrad rms |  | 
Height error | <0.30 nm rms |  |  | <0.30 nm rms |  | 
Corus nanoImag works at 3 discrete energies, and can use ML coatings to increase the incidence angle (NA) and reduce the spot size.
17 x 12 nm2 fwhm
DL = 7 nm fwhm

## Slide 16
CORUS will provide nanoimaging, element mapping and chemical speciation capacity in 3D for biological tissue samples of up to 1 mm3 and for cultured cells and organoids.
The beamline will facilitate running correlative multimodal experiments that interrogate the same sample with multiple imaging techniques, either at the same beamline or elsewhere.
Tissue-scale systems biology (nanoimaging XNH):
neuroscience, cancer, host-pathogen
Cell-scale systems biology:
Pharmacokinetics (XFM), pharmacodynamics (XAS)
Zhang, Bosch, …, Pacureanu, Schaefer. BioRxiv 2025.
https://doi.org/10.1101/2025.04.24.650439
Bosch et al. Nat. Methods 2025
https://doi.org/10.1038/s41592-025-02891-0
Pushie et al. Metallomics 2022. https://doi.org/10.1093/mtomcs/mfac032
Victor-Lovelace and Miller. Metallomics 2022
https://doi.org/10.1093/mtomcs/mfac093
KPIs:
target: 1 mm3 connectome, acquisition 1 month
day0: 1/10 mm3 connectome, acquisition 1 week
Flux 7.6 x 1011 ph/s on sample at 27keV
Flux 4.58 x 1012 ph/s on sample at 19 keV
KPIs:
Flux 2.24 x 1013 ph/s on sample at 10 keV
nanoImag @ RT
nanoFluoSpec @ cryo
Corus

## Slide 17
nTiles < 1000
Acquisition < 1 month
E = 27keV
nanoImag Detector
large Area Detector (>5k width, uncorrelated pixels)
fast frame rates (kHz)
Very long Hutch (ca. 20 m)
Direct Detection (large pixel)
GaAs,CdTe

## Slide 18
Contract follow up | Date
 Contract signed | done
 Kick off meeting | done
 Basic project | Under evaluation
Executive project | End July 2026
Review by MICIU | 3 months
Handover to Parc de l’ALBA | Oct-Nov 2026
Execution by Parc de l’ALBA | Jan 2028
Transfer lines Project in progress

## Slide 19
CoDI / Corus Schedule
The schedule of the long beamlines is limited by the delivery of their Buildings (Dec 2030). For Corus we need to decommission MSPD first.
The goal is to start Commissioning CoDi immediately after the dark period.
Corus comes a few months behind.

## Slide 20
ALBA does not have personnel to start all projects immediately, so some projects will start later, and the program will spread in time beyond the opening of ALBA II.
The program schedule follows these considerations:
All exp. techniques available on ALBA II day one We want to assure that all our current beamlines will be able to open immediately after the dark period, in good conditions and adapted to the new machine (even if not optimal). At least all exp. techniques. This means that also critical upgrades, to allow us continuing operation until the dark period, are also scheduled immediately.
Commitments with User Community ALBA will honor its commitments with the user community, concerning new beamlines.
Minimize downtime of existing beamlines We want to avoid shutting down any beamline for more time than the dark period, or at least minimizing their downtime. Therefore, leaving smaller actuations, that don’t require a long BL shutdown, for later.
MSPD2 | MSPD2 | OPRs |  | 
CODI | CODI |  |  | 
CORUS | CORUS |  |  | 
CALIMA | CALIMA |  |  | 
MISTRAL2 | MISTRAL2 |  |  | 
MISTRAL | MISTRAL-U2 | MISTRAL-U3 |  | 
XALOC | RESTART | XALOC-U1 |  | 
XAIRA |  | XAIRA-U1 | OPRs | 
3SBAR |  | 3SBAR-U1 | OPRs | 
MINERVA |  |  |  | 
CIRCE |  | CIRCE-U1 | CIRCE-U2 | OPRs
FAXTOR |  | FAXTOR-U1 | OPRs | 
CLAESS |  | CLAESS-U1 |  | 
LOREA |  | CRYO | LOREA-U1 | 
BOREAS |  |  | BOREAS-U1 | 
NCD |  | NCD-U1 | NCD-U2 | 
NOTOS |  | NOTOS-U1 |  | 
MIRAS |  | MIRAS-U1 |  | 
IMM | BET-LABS | BET-OPT | BET-NANO | BET-INT
JEMCA | EM04 |  |  | 
Must start soon
Before Dark Period
No BL downtime required
Flexible scheduling
Beamline Upgrade projects

## Slide 21
Only projects starting in 2026 (or early 2027) are scheduled.
We complete MSPD2, RESTART and NOTOS U1 (=all exp-tech available)
We start the long BLs right after the dark period.
The development of the rest of projects will extend beyond the dark period
Overall schedule

## Slide 22
Projects started in 2026
Modify the endstation of NCD to allow it doing coherent imaging experiments, as a pilot for CoDi, and Corus.
        Ensure all experimental techniques are available after the dark period, Ensuring BLs reach their base performances at the new machine
Procurement of a new TXM microscope with advanced features for Biology and modify the BL accordingly. Solving reliability issues, and Including a high degree of automation.
Realignment of NOTOS to adapt it to the geometry of ALBA II.
Modify the optics to allow operation in an extended energy range
RESTART
MISTRAL-U2
NOTOS–U1
NCD-U1
New CryoTEM for Life science application, including the building to host it.
EM04
Cryogen-free cryostat for the MARES and ARPES stations, to guarantee operation in shortage of LHe.
CRYO
        Instrumentation for the catalysis lab
BET-LABS
Improvements of the optics metrology instrumentation
BET–OPT

## Slide 23
RESTART
1. Adapt beamlines to Geometric changes of the source
ID: source position changes only in z (longitudinally)
Beamline | Description | Position change
BL01-Miras | New extraction system is needed. | n.a.
BL04-MSPD | Moved to port BL33. | n.a.
BL06-Xaira | In line, moves upstream | ∆z = –453,20 mm
BL09-Mistral | Source point chosen to point at the center of M2 | ∆z = 0 ∆θM2 = +0.0731º
BL11-NCD | In line, moves downstream | ∆z = +346.20 mm
BL13-Xaloc | In line, moves upstream | ∆z = –107.00 mm
BL15-3Sbar | In line, moves upstream | ∆z =–453,20 mm
BL16-Notos | Source point chosen to be at the center of the bending magnet | ∆x’ = +0.69º ∆x_MAX = 356 mm
BL20-Lorea | Source moves downstream | ∆z = +453,20 mm
BL22-Claess | Source moves upstream | ∆z = –644.83 mm
BL24-Circe | Source moves upstream | ∆z = –453,20 mm
BL25-Minerva | Source point chosen to point at the center of M1 | ∆z =+121.42 mm ∆θM1 =+0.14º
BL29-Boreas | Source moves downstream | ∆z = +453,20 mm
BL31-Faxtor | Source point does not move | ∆z =0
BL33-MSPD2 | Source moves upstream | ∆z = –453,20 mm
BM: (SXR) we select the extraction angle where the beam points to the first mirror of the BL, the rest of the beamline does not need realignment.

## Slide 24
RESTART
Procurement of aging/failing components that risk BL operation
Monochromator (CLAESS)
3 Area Detectors
1 Fluorescence Detector
Slits
Diagnostics
Fast shutters
2 benders
Identification and replacement of obsolete components that would limit the performance in the new machine.
Requirements on mechanical stability become more demanding
Beam heterogeneities at XALOC with the current mirrors
Beam heterogeneities at XALOC with the state of the art mirrors

## Slide 25
Higher flux density on sample
Performance of (some) BLs will be drastically boosted
Lower power on Optics
More uniform beam for a wider range of beam sizes
Smaller reachable spot size

## Slide 26
1
x14
x48
Beamline Enabling Technology
Xaira@ALBA
Xaira@ALBA II
Xaira@ALBA II
Superpolished mirrors
Spot size on sample for XAIRA, at ALBA, at ALBA II with its current optics, and with state-of-the art optics
Advances comes from paradigmatic changes (research and testing)
Adaptive optics, deterministic polishing
Feedback mechanics, parallel robots, complex motion trajectories to simplify mechanics.
Low-level experiment orchestration
AI assisted experiments.
Beamline performance depends on instrumentation technology.
Better optical quality on mirrors, gratings, lenses
Higher mechanical stability and accuracy
Faster detectors
Faster experiment synchronization.
More automation
Data processing

## Slide 27
The nanomotion lab
Notes: Clean room + Superquiet room
Experiment setup inside, electronics outside if posible, route through feedthrough to racks
Experiment control from CR + tests when cleanroom is not required

## Slide 28
Example 2: Runout control
± 112 nm
± 18 nm
Ideal trajectory
Measured runout uncorrected. Results are used to calculate the necessary XY displacements for correction.
Once the XY displacements are activated, measured runout is considerably reduced.
Nanometric sample spot require rotation with nanometer accuracy. Runout can move the sample out of the beam. .

## Slide 29
Quality of optics
Facilities need a laboratory capable of setting up optics with surface accuracy below 1nm.
24 channel superpolished bimorph mirror measured at ALBA.
Calibration profiles (unit response per channel)
Final error to the nominal ellipse.
Residual error 67 pm

## Slide 30
Final Remarks
The Experiments Program includes new beamlines and upgrades of all existing beamlines.
The process will extend in time, beyond the dark period, but the downtime of experimental techniques will be minimized.
The new source, and state-of-the-art technology bring opportunities for the experimental stations: Faster, In-operando, high-throughput, Diluted, etc.
ALBA will boost its capacities in Coherent Imaging techniques, with a smaller source, longer beamlines, and target upgrades of existing BLs.