ALBA-II Lattice Design
robustness and performances with Simulated Commissioning
G. Benedetti
O. Blanco, M. Carlà, Z. Martí
HEPS-ALBA workshop – 13-14 July 2026

---
The ALBA-II lattice team
- Gabriele Benedetti: coordination, lattice design, injection
- Oscar Blanco: lattice design, non-linear optimisation, errors, injection, AT development
- Michele Carlà: lattice design, non-linear optimisation, UFO development, injection
- Zeus Martí: errors, tolerances and correction, commissioning, AT development

---
Outline
- ALBA at present, constraints and requirements for ALBA-II
- The 5BA cell for ALBA-II and pseudo 16-symmetry solution
- Injection scheme and optics for the injection section
- Lattice optimization process with UFO and NSGA2
  - Dynamic and Momentum Apertures
- Robustness and performances with errors evaluated with Simulated Commissioning
  - Injection efficiency and Touschek Lifetime

---
ALBA 2025
ALBA facility in 2026
13 operating beamlines + 1 in 2027
3 electron microscopes
Instruments for life science
FAXTOR
Instruments for material science
BOREAS
MIRAS
Instruments for metrology
MINERVA
CIRCE
MSPD
CLAESS
3 GeV Booster 249 m
LOREA
XAIRA
3 GeV Storage Ring 268 m
Cryo-EM
MISTRAL
InCAEM
TEM
NOTOS
NCD-SWEET
XALOC
3SBAR
110 MeV linac

---
Constraints, requirements for ALBA-II
Requirements:
- Emittance < 400 pm·rad
- Straight sections length > 4 m and βx*≈ βy*≈ 2 m
- Dynamic Aperture > 6 mm for off-axis injection → small tune shift with amplitude
- Lifetime > 10 h → full coupling + large momentum acceptance → small tune shift with energy
- Injection efficiency of 100%
Constraints:
- Preserve 12 ID source points + SR circumference → 3 different lenghts for straight sections
- Keep energy 3 GeV
- Re-use current booster 10 nm·rad
- Vacuum chamber aperture ~ 16 mm
  - Reverse bend gradient < 70 T/m
  - Quad gradient < 100 T/m
  - Octupoles < 7·105 T/m3
  - Sextupoles < 5000 T/m2

---
Choices for the ALBA-II MBA lattice
1. Lattice based on 5 Bend Achromat cell with distributed sextupoles
   (G.Benedetti, et al. Status of lattice studies for ALBA-II. IPAC’26)
2. Developing a lightweight, fast and efficient tracking code running on GPUs (UFO) to speed-up the evaluation of lots of lattices
   (M.Carlà. UFO, a GPU code tailored toward MBA lattice optimization. IPAC’22)
3. Injection scheme based on on-energy off-axis technique with a non-linear kicker (G.Benedetti, et al. A double-dipole kicker for off and on-axis injection into ALBA-II. IPAC’22)
4. Increasing Touschek lifetime working with an AC skew quadrupole tuned at Qx-Qy
   (M.Carlà, et al. Phys.Rev.Accel.Beams, vol. 28, p. 082803, Aug. 2025,
   and dedicated talk by Michele Carlà in this workshop)
5. Test performances and robusteness of the lattice with the Simulated Commissioning toolkit (T.Hellert, et al., Phys.Rev.Accel.Beams, vol. 25, p. 110701, Dec. 2015)

---
The 5BA cell
Arc:
5 bends with transverse gradient: QD/QDS
8 anti-bends: QF/QFS
11 sextupoles: 4 SH + 7 SV
7 octupoles/skew quads: OV
Matching section:
4 quads: Q1/Q2/Q3/Q4
3 octupoles: O1/O2/O3
3 different straight section lengths:
Same arc for the 16 cells, three different lengths of the straight section to match the the existing beamlines

---
Pseudo 16-periodic lattice (A2L007d)
All the straight sections have low betas, but the injection section is asymmetric to produce low βx at the thin septum and high βx at the DDK kicker
16 cells with 3 different straight section lengths 5.2 m / 4.6 m / 3.9 m and same phase advance
16-fold symmetry (on-energy), 16 cells, 3 different straight lengths = 4.7m / 3.5m / 4.4m
Emittance: 200 pm·rad (154pm·rad / 77pm·rad @50% coupling)
Mom. Compaction: 1.1·10-4
βx at SS: 4.1 / 2.9 / 3.6 m
βy at SS: 1.9 / 1.6 / 1.8 m
Tunes: 38.17 / 13.28
Chromaticity: -100 / -35

---
Pseudo 16-fold symmetry on- and off-energy
To obtain 16-fold periodicity:
The arcs of the 16 cells are identical
For on-energy periodicity:
- 16 matching sections, included the injection one, tuned to the same phase advances
For off-energy periodicity
- 16 matching sections, injection included, with horizontal chromatic amplitude function (Wx) matched at the ends

---
Main params of the storage ring A2L007d
LATTICE	ALBA	ALBA-II A2L007d
Energy	3	3	m
Emittance ε0 (εx/ εy w/ IDs and 50% coupling)	4500	200 (154 / 77)	pm·rad
Tunes	18.15 / 8.36	38.17 / 13.28
Chromaticity	-39 / -29	-100 / -35
Mom. compaction	8.9·10-4	1.1·10-4
Energy spread	1.0·10-3	1.2·10-3
Energy loss/turn	1025	925	keV
Damping times	4 / 5 / 3	3 / 6 / 7	ms
Lifetime @ 250 mA, 0.5% coupling	20	...	h
Lifetime @ 300 mA, 50% coupling, HC	...	10	h
Straight section length	7.8 / 4.2 / 2.3	5.2 / 4.6 / 3.9	m
βx at straight centre	2.0	4.1 / 3.6 / 2.9	m
βy at straight centre	1.8	2.0 / 1.8 / 1.6	m

---
Optics for the injection section
Injection section is a modified Long straight: low βx at septum, high βx at DDK kicker
Standard Long straight sections: betas with symmetric waist.
Two of them are used for the RF cavities and one for a beamline.
Medium and Short straight sections are similar to the Long one: all matched to have the same phase advance.
The phase advance is kept equal to all the other 15 straight sections
→ quasi 16-fold symmetry
G. Benedetti, et al. Progress on the 5BA lattice for ALBA-II. IPAC’25.
THIN SEPTUM
DDK

---
Magnets arrangement in the injection straight
All the magnets for the injection must be installed in one of our longest straight section which is only 5.2 m long.
2 thick septa (permanent magnets)
1 thin septum (pulsed)
1 pulsed non-linear kicker (DDK)
The low βx at SE-THIN allows reducing the aperture of the thin septum → injected beam closer to the SR axis (-9 mm) → lower DDK kick
The high beta at DDK magnifies the dynamic aperture to more than 6 mm to allow off-axis injection at -5 mm

---
DDK: Double-dipole Kicker
The DDK is a novel pulsed non-linear kicker developped at ALBA:
 switching 4 inner rods off
 switching 4 outer rods off
 powering 4 inner + 4 outer rods
Switching off either the inner or the outer rods, a dipole field is produced.
A dipole is needed for on-axis injection during the ALBA-II commissioning.
ALBA-II straight sections have very little room and combining two kickers in one will be very useful.
A prototype of the DDK has been produced and successfully tested in ALBA in 2026.
(R.Muñoz, et al. Development and characterization of the double-dipole kicker prototype at ALBA. IPAC’26)

---
Lattice Optimization with UFO and 2 objectives
- Input is only the linear optics (tunes, betas at straights, drifts btw elements)
  - Systematic multipoles in anti-bends (QF, QFS) are included since they are the strongest ones
  - Initially, chromaticity corrected with 2 sextupole families, and 20% of the tune shift with horizontal amplitude with octupoles
- Tracking with UFO: 2 objectives NSGA2 algorithm for Python:
  - Used small random position errors per magnet (smaller than commissioning errors)
  - Calculate the 2 objectives: Dynamic Aperture and Touschek Lifetime
- Initial fast evolution (~2-3 hours) of about 100 generations with low population (100 rings), including :
  - Sextupole and Octupole ranges from 80% of initial value to maximum limit
  - Compare and evaluate the best solution
  - Cross-checking D.A. (“Flood Field” method) and Lifetime with AT2 code
- Keep optimising after adjusting ranges for a larger number of generations and population (typically 1000 rings per generation)
- Iterate increasing the number of sextupole and octupole families
  - Initial number of families: 11 sxt, 9 oct.
  - Final number of families: 33 sxt, 9 oct.
- The entire optimization process takes ~1-3 days

---
Rhomboid vacuum chamber physical apertures
Rhomboid vacuum chamber H/V aperture = 20/14.8 mm
(courtesy R.Parise)
Asymmetric absorbers
Hor : +8 mm
Optimization and checks are calculated with these physical apertures.

---
Lifetime and crossing of resonance stopband
Touschek particles at +2.5% can cross the half-integer resonance without being lost if the passage is fast and the resonance stopband is sufficiently narrow
From +2.5% to +3.5% there is a small change in acceptance with a big contribution to Touschek lifetime.
For the lattice A2L007d case w/ HC and errors:
lifetime crossing νx= 0.5 is 15 hours, cutting at νx= 0.5 reduces to 11 hours
Only if our model of errors and corrections is very complete, particles crossing the stopband can be taken into account for lifetime.
Therefore, we will take as educated guess the lifetime estimation cutting the energy acceptance when νx=0.5.

---
Dynamic and momentum aperture
Frequency map at DDK
DA at the DDK
w/ phys. aper.
X-Energy acceptance
Tune shift with Energy
DA reaches -8 mm, which means the limit of the physical aperture
Momentum aperture renders a Lifetime of 10 hours.

---
SC a tool for ALBA-II
The robustness, required correction budget and performances of the lattice are evaluated with the Simulated Commissioning Matlab toolkit (SC)
lattice
Expected performance
Simulated
Commissioning
orbit/optics correction scheme
expected errors
Required orb./opt. corr budget
injected beam
iteration until satisfactory performance, tolerances and budgets are achieved

---
Correction Scheme
- 11 BPM/Sector. BPM before and after QD to allow fast angle polarization swich for beamlines (FaPS) .
- H/V orbit corrector magnets (HCM and VCM) are integrated in octupoles and sextupoles. Total 11 CM per plane and sector.
- Quads quadruplet (Q1/Q2/Q3/Q4) in the matching sections have independent power supply.
- Combined Function dipoles (CFD) QF, QFS and QD as optics knobs. Each magnet has a single power supply, used to correct the focusing errors, the combined dipole error is corrected with the HCM. QDS (permanent magnet) are not used for optics correction.
- Arc BBA performed with the skew quads embedded in the octupoles. Extra skews will be used to correct the DC coupling.
- IDs corrected with matching quadruplet, QF and QFS.

---
Commissioning simulations steps
DURING ON AXIS INJECTION:
- Improve initial transmission. (Goal : 1st turn)
  - Injection correction (3 BPM+BBA)
  - Perform trajectory corrections to reach one BPM at the time up to 1st BPM, 1st ARC, and 1st turn.
  - Perform correction to reach a 2nd turn.
  - Injection is now more realistic, starts at the Septum exit and includes a pulsed DDK.
  - Pre-BBA offset relaxation (a la M.Aiba).
- TbT BBA (Goal : Reduce large unknown offsets in BPMS)
  - Steer the beam through quads in the straights to estimate the BPM offsets in the straights
  - Steer the beam through skew quads in sextupoles to estimate the BPM offsets. In the arc.
  - Maybe not needed if BPM offset error < 300 μm.
- Injection beam static error correction (Goal: Improve beam transmission in few turns)
  - Identify and correct any mismatch at injection
  - Removed since we noticed it tends to go towards unrealistic corrections.
- Sextupole (and octupole) ramp-up (Goal : Reduce sensitivity to energy loss/energy gain)
  - Ramp up the sextupoles in steps to their nominal values while correcting the orbit
- Main RF commissioning (Goal : Improve beam transmission over hundreds turns)
  - Several cavities are included, synchronization step added.
  - Turn on the main cavities. Correct the phase and frequency while improving the beam transmission/signal.

---
Commissioning simulations steps
- TbT average orbit correction (Goal : Profit from ~1000 turns)
  - Since we use the new 1fold lattice, some seeds that have >1000 turns do not have closed orbit.
  - A proxy for the closed orbit correction is the TbT average orbit correction.
  - Not needed if we manage to correct injection trajectory...
- BEAM HAS BEEN CAPTURED:
- Closed Orbit Correction (Goal : Profit from better BPM readings to increase the stored current)
  - Measure Response Matrix. Correct the orbit to improve injection current. Check DA.
- Closed Orbit BBA (Goal : Reduce the BPM offsets to values adapted for LOCO)
  - Steer the beam through quads in the straights to estimate the BPM offsets in the straights
  - Steer the beam through skew quads in sextupoles to estimate the BPM offsets. In the arcs
  - Repeating the BBA with all triplet/quadrupled quads and combine the results is more precise.
  - Correct the orbit.
- LOCO optics correction (Goal: Recover enough DA and MA for off-axis injection)
  - Use loco to reduce beta-beat, restoring tune, and the expected dynamics of the ring.
  - New formula for the orbit response matrix derivative.
  - An offset relaxation is applied at every LOCO step.
- AC skew quad stripline simulations to crosscheck 50% coupling.

---
SC input errors table
The SC input expected errors (2σ cut) have been estimated together with other teams:
Also the alignment technique is taken into account:
(dedicated talk by Marta Llonch in this workshop)
MAGNETS	QD/QF	Q1/Q2/Q3	CORR	SEXT	OCT
Dipole calib.	0.1 %			5%
Corr limit			0.5 mrad	1.0 mrad
Quad Calib.	0.07%	0.07%			0.07%
Skew limit					0.15 T
BPM
Calibration	5%
Noise (TbT / CO)	200 / 1 μm
Offset	200 μm
Roll	4 mrad
RF
Frequency	0 (100Hz?)
Voltage	0.1%
Phase	90º
Injected beam (x,x’,y,y’,δ,ct)
Beam size	300 μm / 70 μrad / 200 μm / 40 μrad / 0.1% / 13 mm
Beam jitter	340 μm / 70 μrad / 100 μm / 40 μrad / 0.01% / 0.2 mm
Beam offset	1 mm / 0.1 mrad / 1 mm / 0.1 mrad / 0.1% / 1 mm
ALIGNMENT	Offsets H,V,L (μm)	Rotations around s,x,y (μrad)
Magnets	31, 31, 31	120, 120, 120
Girder	61, 61, 0	50, 0, 0
Circumference	0.63 mm
1
1
2
2
3
A
A
B2
B1
C

---
Optics correction with Combined Function Dipoles
The ALBA-II lattice has 208 CFD and 176 of them are used to correct the optics.
The magnetic design for the CFD has a single power supply.
The optics correction implies gradient+dipole changes → it must be taken into account together with the orbit correction and a small energy change
- 6D simulations of optics+orbit correction have confirmed that the CFD with single power supply design works well.
- An optics correction iteration based on standard LOCO with numerical calculation of the Orbit Response Matrix Jacobian would take ~30min.
- At ALBA we have developped an analytical version of LOCO for the CFD which takes few seconds.

---
Performances with errors
With Simulated Commissioning Injection efficiency, horizontal Dynamic aperture and Lifetime are evaluated for 100 error seeds.
The Cumulative distribution function (cdf) is used to show the statistics and robustness of the performances.
Injection efficiency > 98.5% and Lifetime > 11 hours for more than 90% of the seeds.

---
Corrections budget
All the correction strengths needed are within the magnetic design ranges.

---
Summary
- Tools and algorithms for lattice design, non-linear optimization and SC: developed, tested and working.
- A baseline lattice (A2L007d) with 5BA cell and pseudo 16-fold symmetry is almost ready to be frozen.
- The dynamic aperture is optimized up to the physical aperture limit of 8 mm
- Injection will be performed off-axis with the current booster and a novel Double-dipole kicker
- The ALBA-II commissioning and operation would be allowed with the following average performances:
  - Injection efficiency > 99%, DA = -7.5 mm, lifetime 11 hours at 300 mA and 3rd H.C.
- Magnets butget for corrections is within design

---
EXTRA SLIDES

---
Beam sizes, coupling and lifetime
Coupling has been fixed at 50% as a trade-off between lifetime (for the machine performance) and vertical beam size (for beamlines)
Beam size with 50% emittance ratio
ex = 160 pm, ey = 80 pm
Touschek Lifetime w/o H.C.:
ibunch=0.00075 A, σs=0.00243 m, σe=0.00126, emit0 = 200 pm
RFCAV : 2 sets of cavities at 1.2MV