## Slide 1: Beam Instabilities and Longitudinal Dynamics in HEPS
Haisheng Xu
ALBA-HEPS Virtual Workshop, July 13-14
July 13, 2026

## Slide 2
CONTENT
Brief Introduction
Studies of Longitudinal Dynamics in HEPS
On-going Studies and Possible Next Step
Summary

## Slide 3
Brief Introduction

## Slide 4: Brief information of HEPS
[1] Y. Jiao et al., J. Synchrotron Rad. 25, 1611–1618 (2018).
[2] Y. Jiao, RDTM 4, 399 (2020).
[3] H. Xu et al., RDTM 7, 279–287 (2023).
Challenging!

## Slide 5: Brief information of HEPS
HEPS storage ring
  “high-bunch-charge mode"
    14.4 nC/bunch (200 mA, 63 bunches)
  “high-brightness mode”
    1.33 nC/bunch (200mA, 680 bunches)
  on-axis swap-out injection scheme + high energy accumulation in booster
    “full-charge bunch” injection --- mismatched injected bunch of 14.4 nC / 1.33 nC;
    injection imperfection induced initial transverse offset;
HEPS booster
  need to provide high charge bunch (>14.4 nC) to the storage ring
  ramping from 500 MeV to 6 GeV
High bunch charge!

## Slide 6: Brief information of HEPS: RF system
Courtesy of Pei Zhang
Active dual-RF system for the storage ring

## Slide 7: Brief information of HEPS
Very small momentum compaction factor: ~
Very low synchrotron oscillation frequency: ~200 Hz
Need to use harmonic cavity to lengthen the bunch!
  More complicated longitudinal dynamics!
Slow longitudinal oscillation!

## Slide 8: More complicated longitudinal dynamics
Double-RF system with active harmonic cavities
  Nonlinear longitudinal motion
  Longitudinal stability when adjusting ID gaps
  Lower synchrotron tune and larger spread
    Synchrotron frequency is in the FOFB bandwidth
High single-bunch charge induced collective effects
  Possible beam induced heating problem
  Bunch distribution distortion because of longitudinal impedance

## Slide 9: Storage ring impedance modeling
The coupling impedance model of the whole ring was developed based on element-by-element computations with analytical formulae or numerical simulations.
Courtesy of Na Wang

## Slide 10
Studies of Longitudinal Dynamics in HEPS

## Slide 11: Longitudinal dynamics w/ and w/o HC
RF potential diff
Haissinski solutions diff
Longitudinal motion
  Linear: w/o HC
  Nonlinear: w/ HC
w/o HC
ideal HC

## Slide 12: Microwave Instability (simulations)
Bunch Length
Energy Spread

## Slide 13: High-Charge Limit in the transient process after injection
Single-bunch 15 nC, initial vertical offset , initial bunch length , initial energy spread
Linear One-Turn Map
Element-By-Element
8
Courtesy of Zhe Duan

## Slide 14: Systematic Study of Collective Effects
Beam parameters at 200 mA design current (including impedance, IBS, etc.)
H. S. Xu, et al., RDTM 7, 279–287 (2023).

## Slide 15: Bunch lengthening commissioning
Manage to reach nearly ideally flat bunch distribution at arbitrary beam current. （~1.2 nC / bunch）~ 3.2 times bunch lengthening
Raw data
10.21 mm
32.51 mm

## Slide 16: 2. Fine tuning of the cavities’ phase
Horizontal average orbit from the BPM turn-by-turn data
Rough tuning the cavities’ phase, we used the turn-by-turn sum signal of one BPM.
Fine tuning the cavities’ phase, we used the horizontal average orbit (trajectory) from the BPM turn-by-turn data as an indicator to calibrate the phase of RF cavities.

## Slide 17: Fine tuning of the cavities’ phase
before calibration
Rough tuning the cavities’ phase, we used the turn-by-turn sum signal of one BPM.
Fine tuning the cavities’ phase, we used the horizontal average orbit (trajectory) from the BPM turn-by-turn data as an indicator to calibrate the phase of RF cavities.
After calibration, the bunch length (at same single-bunch current) became shorter.
after calibration
9.48 mm
7.19 mm

## Slide 18: Longitudinal Coupled-Bunch Oscillation (CBM0)
振荡幅度约 168 mm

## Slide 19: Mode analysis with bunch-by-bunch feedback
With mode zero instability
  Mode zero arises and results in beam current threshold
LLRF kp=1 @56mA
Mode=0
Mode=62
Mode=0
Mode=62
LLRF kp=4 @60mA
Without mode zero instability
  Several modes with much lower amplitude, the mode zero is not dominated

## Slide 20: Instability growth time measured from FA data
Slow instability with the fitted growth time of ~1.2 s (without counting the synchrotron radiation damping), indicating that the growth time of this instability is approximately 18.4 ms.
Likely coupling between coupled bunch instability and slow tuning mechanisms.
Dipolar oscillation dominated with many higher order sidebands.
Beam loss
Fitted growth time  1.2 s
Harmonic RF cavities detuned to around 70kHz~100kHz

## Slide 21: Mitigation strategies
Tuning the kp parameter of the cavity LLRF can damp the mode zero instability
Bunch-by-bunch feedback can provide extra damping to the instability
Since the synchrotron frequency is quite low (less than 100 Hz), FOFB show damping effects on the coupled bunch modes (without zero mode).
Oscillation amplitude with FOFB on
FOFB off

## Slide 22: Dedicated beam time for studying the CBM0
Kp of 166.6 MHz cavities
Kp of 499.8 MHz cavities
63mA, stable
Amplitude of the peak at ~10
Amplitude of the peak at ~1000
95mA, unstable
Beam current
amp
amp

## Slide 23: Cavity field & resonance control: I/Q
IQ vector control (field)
- Sample ref. & pickup signals
- Non-IQ demodulate to IQ
- IQ errors to PI controller
- DDS output IF drive signal
IQ vector control (resonance)
- Sample fwd. & pickup signals
- Demodulate to IQ -> phase error
- SC cavity tuner: Motor & Piezo
- NC cavity tuner: Motor
Courtesy of Qunyao Wang

## Slide 24: A different LLRF control strategy of the HC
This scheme was tested and verified!
More efforts needed to make it operates more stable.
Ib =24.5mA
Pb =-15kW
Vc =1.25MV
Vb =0.13MV
Vg =1.20MV
φs =240°
Ignasi Bellafont, talk in the 9th Low Emittance Rings Workshop, CERN, 2024
F. Perez, et al., NIMA, 2025.

## Slide 25
On-going studies and possible next step

## Slide 26: On-going studies
Control strategy of the HCs at high beam current
Operation strategy when ID gaps changing （U0 feed-forward table）, how to operate two HCs stably；
Trying to find out the physical reason of CBM0;
Cure the mode 0 via algorithm and a mode 0 damper;
Studying the longitudinal coupled-bunch instability;
Carrying out experiments of collective beam instabilities with active harmonic cavities and cure them;
Influences of FOFB on longitudinal collective motions.

## Slide 27
Summary

## Slide 28: Summary
Systematic studies of longitudinal dynamics were carried out in the design stage of HEPS.
Commissioning of double-RF system were quite smooth at the beginning to reach ideal-lengthening. However, more attention was paid to increase beam current and operate the machine stably (HC setup and ID gaps; stabilize the HC synchronous phase, etc. )
More experimental studies of longitudinal dynamics in HEPS are planned in the future machine shifts.
Possible next step:
  U0 feedforward;
  Keep increasing beam current towards the designed current 200 mA;
  keep stable operation at high current (e.g, find out the physical reason of CBM0);
  mode 0 damper (algorithms is under test and would be tested in the next run);
  experiments of collective beam instabilities with active harmonic cavities;
  ……

## Slide 29: Thank you!