## Slide 1: Vacuum system design and prototyping ALBA-HEPS Workshop Ricardo Parise, on behalf of the ALBA01-WP2 and the ALBAII WP20102 working groups 14/07/2026
rparise@cells.es

## Slide 2: Table of contents ALBA01 Prototyping: 6BA Lattice Vacuum chambers prototypes Vacuum chamber prototypes testing setup ALBAII: Lattice A2L007c Vacuum system overview Dipole chamber design Chamber cross section Synchrotron power
14/07/2026
ALBA-HEPS Workshop

## Slide 3: ALBA01 Prototyping: 6BA Lattice
Vacuum chambers prototypes
Short dipole chamber prototype
Long dipole chamber prototype
Vacuum chamber prototypes testing setup

## Slide 4: ALBA01 Prototyping: 6BA Lattice Vacuum chamber prototypes status: Recapitulating…
14/07/2026
4
ALBA-HEPS Workshop

## Slide 5: ALBA01 Prototyping: 6BA Lattice Vacuum chamber prototypes: QDS
Conical absorber:
Shadows gaskets and BPM;
Smooth 1:10 slope
6
"Straight-ish" electron beam path
One aperture to fit them all: unified design for
all ID beamlines
7-8 mm vertical aperture: needed to extract the ID light
ALBA-HEPS Workshop
14/07/2026

## Slide 6: ALBA01 Prototyping: 6BA Lattice Vacuum chamber prototypes: QDS
6
Brazing
Integrated cooling circuit
Solid machined parts
Brazing joints detail
Solid machined parts
Designed to fit the magnets (Quad. and Sext.)
Integrated cooling circuit
1
2
3
4
5
6
1
2
3
4
5
6
ALBA-HEPS Workshop
14/07/2026

## Slide 7: ALBA01 Prototyping: 6BA Lattice Vacuum chamber prototypes: QDS
6
ALBA-HEPS Workshop
14/07/2026

## Slide 8: ALBA01 Prototyping: 6BA Lattice Vacuum chamber prototypes: QDS
QDS Chamber
OFHC-Cu
Brazed flanges
Conventional ABS
NEG coated
Design phase Finished
FDR Approval Finished
Material procurement Finished
Manufacturing Finished – Issues during EDM
Brazing – 1st step Finished – Took longer that expected
Milling Finished
Brazing – 2nd step On going
TIG welding (flanges) Jul. 26
NEG coating Sep. 26
FAT Sep. 26
Delivery Oct. 26
SAT Nov. 26
5
ALBA-HEPS Workshop
14/07/2026

## Slide 9: ALBA01 Prototyping: 6BA Lattice Vacuum chamber prototypes: QD
7
Distributed absorbers
Curved beam, straight path
Curved beam, polygonal path
Minimum material removal: making space for QF without losing much strength
Constant 3mm vertical aperture
Minimum 1mm wall thickness
Distributed cooling
6mm vertical antechamber
Increasing wall thickness
ALBA-HEPS Workshop
14/07/2026

## Slide 10: ALBA01 Prototyping: 6BA Lattice Vacuum chamber prototypes: QD
7
EB Welding
Solid machined parts
Integrated cooling circuit
Cooling: Low-temperature brazing alloy + clamping
Round tube
ALBA-HEPS Workshop
14/07/2026

## Slide 11: ALBA01 Prototyping: 6BA Lattice Vacuum chamber prototypes: QD
8
ALBA-HEPS Workshop
14/07/2026

## Slide 12: ALBA01 Prototyping: 6BA Lattice Vacuum chamber prototypes: QD
QD Chamber
CuCrZr
No brazing
Integrated ABS
NEG coated
Design phase Finished
FDR Approval Finished
Material procurement Finished
Manufacturing Finished
Cooling unit Finished
EB-Welding tests On going
EB-Welding Jul. 26
NEG coating Sep. 26
FAT Sep. 26
Delivery Oct. 26
SAT Nov. 26
7
ALBA-HEPS Workshop
14/07/2026

## Slide 13: ALBA01 Prototyping: 6BA Lattice Vacuum chamber prototypes testing setup
By Juan Carlos Giraldo, from Project Office
11
ALBA-HEPS Workshop
14/07/2026

## Slide 14: ALBA01 Prototyping: 6BA Lattice Vacuum chamber prototypes integration setup
By José María Álvarez, from Project Office
12
ALBA-HEPS Workshop
14/07/2026

## Slide 15: ALBAII: Lattice A2L007c
Vacuum system overview Dipole chamber design Chamber cross section Synchrotron power

## Slide 16: ALBAII: Lattice A2L007c Vacuum system overview
14
Per arc:
1 vacuum section (2 gate valves)
5 dipole chambers in some Cu alloy, NEG coated, ex situ activation
5 pumping locations
5 crotch absorbers + distributed absorbers
11 BPMs
7 standalone (BPM + bellows)
4 integrated in the dipole chambers
Minimum one bellows between every two BPMs
ALBA-HEPS Workshop
14/07/2026

## Slide 17: ALBAII: Lattice A2L007c Vacuum chambers design
18
MO 25
Dipole chambers
Cu alloy: OFS-Cu, CuCrZr
Rhombic cross section
Integrated cooling and absorber
Integrated BPMs
Block for pumping + crotch absorber
MO and/or CF flanges
NEG coated
Ex situ activation
KF25 clamp
MO25
CF25
CF 25
with cooling
ALBA-HEPS Workshop
14/07/2026

## Slide 18: ALBAII: Lattice A2L007c Chamber cross section
Previously planned: 16 mm circular aperture
Injection studies required larger horizontal aperture
Magnet poles remained fixed
Minimum 1 mm chamber-to-magnet clearance
Main geometric constraint: Available chamber envelope
14
ALBA-HEPS Workshop
14/07/2026

## Slide 19: ALBAII: Lattice A2L007c Synchrotron radiation total power
How to deal with those power?
Antechamber and crotch absorber;
Distributed absorbers (chamber walls);
“Conical” absorbers
 |  | QDS | QD | QFS | QF
Energy | [GeV] | 3 | 3 | 3 | 3
Current | [mA] | 350 |  |  | 
Field | [T] | 1,06 | 1,04 | 0,48 | 0,51
Length | [mm] | 605 | 1050 | 160 | 160
Angle | [deg] | 3,67 | 6,26 | 0,44 | 0,46
Power | [kW] | 2,71 | 4,54 | 0,15 | 0,16
 |  | Cell |  |  | 
# per cell |  | 2 | 3 | 4 | 4
Per magnet type | [kW] | 5,4 | 13,6 | 0,6 | 0,7
Total Power | [kW] | 20,3 |  |  | 
 |  | Ring |  |  | 
# of cells |  | 16 | 13,8 | 0,6 | 0,7
Total power | [kW] | 324 |  |  | 
19
ALBA-HEPS Workshop
14/07/2026

## Slide 20
rparise@cells.es