## Slide 1
Jul 14th, 2026
mllonch@cells.es
ALBA II ALIGNMENT STRATEGY
Marta Llonch On behalf of ALBA Survey and Alignment group: Jon Ladrera Marta Llonch

## Slide 2: Outline
1. INTRODUCTION
2. ALBA II ALIGNMENT REQUIREMENTS AND UNCERTAINTY
3. ALBA II ALIGNMENT STRATEGY
4. ALBA LONG TERM DRIFT
5. SUMMARY

## Slide 3: Introduction
ALBA II Storage Ring
268m circumference
16 arcs of 13m
5 girders per Arc: 80 girders
760 magnets
18mm diameter of Vacuum chamber
Testing PDR DDR CfT Contract Production Procurement
2026
2027
2029
2028

## Slide 4: ALBA II alignment requirements and uncertainty
ALBA II Alignment requirements
Parameter | ALBA II |  | BESSY III | Diamond II | Diamond II | MAX 4U | MAX 4U | Soleil II | Petra IV | Soleil II | Units | Units
Girders |  |  |  |  |  |  |  |  |  |  |  | 
Girder-to-Girder Alignment | TBD* |  | 50 |  | 150 |  | 50 | 100 | 100 | 50 | mm rms | mm
Elements within a girder |  |  |  |  |  |  |  |  |  |  |  | 
Magnet to magnet | TBD* |  | 30 to 50 |  | 30 |  | 25 | 30 | 30 | 30 | mm rms | mm
Standard MPE for Vacuum and Diagnostic component alignment | TBD* |  | - |  | - |  | - |  | - | - |  | mm
Beam Dynamics determines how magnets and girders mechanical misalignments affect the beam quality and the machine performance. Alignment requirements define the maximum positioning errors that the accelerator optics can tolerate while still meeting performance goals (emittance, orbit stability, injection efficiency, dynamic aperture, etc.)
ALBA II alignment tolerances are being determined by introducing estimated alignment uncertainties. This provides a more realistic approach to simulate the alignment process itself instead of assigning arbitrary magnets and girders offsets.

## Slide 5: ALBA II alignment requirements and uncertainty
Alignment uncertainty
Alignment is not a sequence of independent tasks, it is a chain in which uncertainty is propagated from component characterization to the final machine geometry.
“Parameter characterizing the dispersion of the values being attributed to a measurand, based on the information used.” (IVM, 4th ed., 2021, JCGM GUM-1:2023)
Uncertainty propagation
Girders
Adjustment system (pushers/shims/wedges). Mechanical tolerances Stability and rigidity. Thermal effects. Transport effects.
Survey Network
Network geometry and distribution of monuments. Measurement uncertainty (Laser Tracker). Adjustment model. Deformation due to weight variation during installation. Environmental effects (temperature, air refraction index…).
Magnets assembly on girder
Adjustment system (pushers/shims/wedges). Adjustment resolution. Stability and rigidity. Open/close magnets. Thermal effects on the assembly lab. Transport effects.
Fiducialization
Magnetic center measurement (Stretched wire, rotating coil…). External references measurement (Laser tracker, probe repeatability). Mechanical tolerances. Coordinates transference between instruments.

## Slide 6: ALBA II alignment strategy
Alignment strategy process flow
Tunnel preparation
Offline components preparation
Installation
1. Components characterization:
Metrology
Magnetic axis determination
2. Components fiducialization:
Functional reference to external fiducials
3. Magnet Assembly and Alignment on Girders:
  Daily/weekly Laser Tracker compensation
Multiple LT stations around each module
Relative alignment verification
4. Preinstallation verification:
As-built girder verification
5. Survey network preparation:
Observation with empty tunnel
6. Girder support elements:
Marking and alignment of base plates
7. Assembled girders installation
8. Survey network re-observation:
Survey network campaign after loaded slab
9. Girders positioning:
Rough alignment before vacuum chamber installation
10. Girders fine alignment
11. As built verification

## Slide 7: ALBA II alignment strategy - Magnets
Fiducialization
Fiducialization ( µm rms) | µm
Stretched wire position determination | 10
Magnetic axis determination | 15
Fiducials reproducibility | 5
Instrument uncertainty | 15
Instrument adjustment | 10
TOTAL | 26
Determines the relation between the effective axis or center of a component (magnetic or mechanical axis) and its external fiducials.
Fiducialization ensures that alignment is based on the functional geometry, rather than the mechanical geometry.
Currently performing first tests on ALBA II stretched wire bench with a recently arrived Q3 prototype. Magnet pre-alignment on bench and first wire position determination with respect magnet fiducials.
QDS - PM prototype is being aligned on the Hall probe measurement system.
ALBA II Status

## Slide 8: ALBA II alignment strategy - Girders
Girder assembly
Top surface planarity characterization, frame and axis definition.
Relative alignment of the magnets magnetic axes.
Define the relationship between aligned magnets and girder reference system.
Reduce the amount of adjustment required in tunnel.
Magnet to girder errors ( µm rms) | µm
Fiducialization | 26
Laser Tracker error (USMN) | 11
Alignment performance | 12
TOTAL | 31
Wall reference monuments
LT stationing for compensation
Module 2
LT stationing for magnet to girder alignment
Floor reference monuments
Magnet storage
Module 1
Assembling area outline
ALBA II Status
Assembly Lab technical specifications | 
Area | 131 m2
Crane load capacity | 7 Tn
Thermal stability | ± 0,5 C°
Area for LT compensation | Yes
Floor and walls reference monuments | Yes

## Slide 9: ALBA II alignment strategy - Girders
Validates girder design
Flatness
Adjustment mechanics
Stable architecture
1st measurements campaign
Prototypes tests
Empty girders
Loaded girders (dummy magnets)
More measurements to be done with dummy magnets properly supported.
Top plane planarity within specifications: flatness ≤ 0,1 mm
Adjustment mechanics movements test X, Y, Z: < 5 µm resolution
Stability test: There is a difference in modal response due to top frame different geometry of ~10%.
Top plane planarity: TBD
Adjustment mechanics movements test X, Y, Z: TBD
3. Stability test: Adding load to a girder to simulate operational conditions maintains the behavior of the modal response but reduce the Eigenmodes values by a 20%.

## Slide 10: ALBA II alignment strategy - Girders
Absolute alignment (tunnel network)
The absolute alignment (survey network) of each girder can produce girder to girder mechanical discontinuities.
ID source points should be placed according new nominal machine circumference. Fixing SS upstream and downstream girders.
Girders between straight sections can be relative aligned.
Low spatial-frequency displacements in nearby girders.
Relative alignment (girder to girder)
Girder alignment errors ( µm rms) | A | B | C
Survey network calculation | 15 | - | -
Laser Tracker localization (to the network) | 50 | - | -
Laser Tracker localization (wrt A) | - | 20 | -
Laser Tracker localization (wrt B) | - | - | 20
Alignment error B wrt A | - | - | 37
Laser Tracker error (USMN) | 11 | 11 | 11
Alignment performance | 29 | 29 | 29
TOTAL | 61 | 37 | 52*
1
1
2
2
3
A
A
B2
B1
C
1. Girders A aligned wrt tunnel network
2. Girders B aligned wrt first and last cell girders
3. Girder C aligned wrt second and third cell girders
*Girder C alignment error expressed with respect to girders A. Girder C would have 37µm error with respect to girder B1 and B2.

## Slide 11: ALBA Long term drift
Tunnel slab vertical movements
Annual Z deformation with respect to the slab averaged plane from 2014
No absolute reference
Sectors 14 and 15 vertical growth
Tunnel altimetric evolution
2024 - 2014
2024 - 2023
Maximum deformation of ± 1.5 mm in Z in 10 years
Maximum deformation of ± 0.5 mm in Z in 1 year
Consistent profiles observed over the last decade and the current year performance, specially in sectors 4 to 8

## Slide 12: ALBA Long term drift
Tunnel slab horizontal movements
Maximum horizontal movements
Tunnel planimetric evolution
Maximum deformation of ± 1.5 mm in X and Y in 10 years
Maximum deformation of ± 0.3 mm in X and Y in 1 year
Consistent profiles observed over the last decade and the current year performance
Long-term deformation impact on the perimeter enlargement of the Storage Ring
Maximum increase in radius of approximately 3.5 mm in X direction since 2008
During operation period (2012 – 2024), the slab has a maximum radius growth of 1 mm in the X direction
Perimeter growth fits with the SR radio frequency decreasing during last years
2024 - 2014
2024 - 2023

## Slide 13: Summary
ALBA II alignment strategy is being developed from alignment requirements down to installation procedures.
Uncertainty propagation is the common framework linking fiducialization, girder assembly, installation and long-term monitoring.
Prototype validation is providing the experimental basis to refine the final alignment strategy.