## Slide 1
U. Iriso (ALBA), C. Carilli (NRAO), B. Nikolic (Univ. of Cambridge), N. Thyagarajan (CSIRO), and L. Torino (ALBA)
Beam Size Measurements using Non-Redudant Aperture Interferometry
HEPS - ALBA Workshop
July 2026

## Slide 2
Introduction: 2-apertures Interferometry
Fourier Domain: from 2-holes to N-holes Interferometry
Non-Redundant Aperture Interferometry
Examples and SRW Simulations
Other Applications: WaveFront Sensing
Conclusions

## Slide 3
Double Aperture Interferometry
Pioneer implementation by T. Mitsuhashi based on Young’s Interferometer (~90s)
Use the synchrotron radiation and a double-aperture mask to produce an interferogram and measure the 1st order spatial coherence.
Typically used in the visible range.
Interference profile from a point-like source
Interference profile from a finite source (s > 0)
Sync Rad from
Magnetic element
SR
Double
Aperture
e-beam
CCD
Lens
Monochromator
Interferogram @Image Plane
Polarizer
~1995
Notes: Coherence already measured by Michaelson ~1900 by measuring the ratio peak/minimum of fringe

## Slide 4
The interference pattern in the image plane follows an analytical expression:
Double Aperture Interferometry
All parameters are known, except the “Visibility” (V)
V obtained by fitting, or simply measuring max intensity and adjacent minima.
From V, the beam size (sx) is obtained using the Van Cittern-Zernique theorem
Imax
Imin
I0 : intensity
a: pinhole radius
D: distance between pinholes
l = wavelength
f: focal length
L: distance to the source
~1995

## Slide 5
SRI limitation: provide only 1d measurement  the 2-aperture orientation defines direction analysis
Using a rotating mask, we can fully reconstruct beam profile by fitting s for different rotation angles
Multiple interferograms (at least 4) need to be done  2D reconstruction not in real time
*L.Torino and U.Iriso, PRST-AB 19, 122801 (2016)
Double Aperture Interferometry: Rotating Mask
~2016

## Slide 6
Coherent amplification of voltages, E
Geometric delays set by electronics
Images made from Fourier Transform
Vi,j = Ei x Ej* = Ai,j, 𝝓i,j
Influence from Radio-Astronomy
~2023
Radio-Astronomy Observatories | Synchrotron Radiation Interferometry
Antennas | Apertures
Radio (GHz) Measurements | Visibilities
Notes: Images made from Fourier Transform of Visibilities

## Slide 7
Influence from Radio-Astronomy
Nant = 27 antennas at the Very Large Array telescope
(NRAO – New Mexico, USA)
Antennas (telescopes)   Apertures
Able to image stars with this shape, why not a Gaussian beam??
 For Synchrotron Radiation Interferometry, working in the Fourier Domain and working with more apertures will have advantages
Nant = 27
~2023
Notes: Q for Chris: This case corresponds to 27 antennas. Is this VLA?

## Slide 8
Fourier Domain: 2-apertures
Raw Image
2D FFT
Auto
0-1
1-0
Ap0
Ap1
Mask
Central Peak: Autocorrelation  V00 I0 + I1
Top peak: Visibility between apertures 0,1  V01 01
I0, I1 : Intensities of apertures 0,1.
V00 and V01 calculated from the (complex) Sum within the circle of the peak
We could fit the two points with a normalized Gaussian in the Fourier (u,v) plane and get the coherence length sC:
The beam size (s) is inferred using VCZ theorem:
s=l·L/(p·sC)
Fourier Domaim (u,v) image:

## Slide 9
Fourier Domain: 3-apertures
→ In Fourier space, we can fit the three points with a normalized 2D-Gaussian and get (σCx , σCy)
 Beam size (σx , σy) using again the VCZ theorem
Auto
0-2
0-1
1-2
Central Peak: Autocorrelation  V00 I0 + I1 + I2
Peak 0,1: Visibility between apertures 0,1  V01 01
Peak 0,2: Visibility between apertures 0,2  V02 02
Peak 1,2: Visibility between apertures 1,2  V12 12
Vij, calculated from the (complex) Sum within the circle of the peak (i,j)!
Raw Image
2D FFT
Mask
sx=l·L/(p·sCx)
Notes: Assuming a flat Gaussian beam, and knowing (I0, I1, I2), or if I0=I1=I2 .

## Slide 10
Fourier Domain: N-apertures
The process can be generalized as:
with
*B. Nikolic, C. Carilli, U. Iriso, N. Thyagarajan, and L. Torino, “Two-dimensional synchrotron beam characterization from a single interferogram“, PRAB, 27, 112802 – Published 25 November, 2024
For N-holes, the Known Parameters, Pk:
  Distinct peaks in the Fourier Domain (visibilities, Vij)
For N-holes, the Unknown Parameters, Pu:
  2D tilted Gaussian: (su, sv, f)  3 unknowns
  Hole Intensities: Gi , for i=1… N  N unknowns
  Joint fit to the measured Vij to obtain both the Gaussian source parameters and hole gains (intensities)
Pu= N +3
System fully characterized if Pk > Pu
So, for 5 holes
Self-calibration Technique*:
Auto
0-2
0-1
1-2
2D FFT
Pk = (𝑁(𝑁 − 1)/2) +1

## Slide 11
Results with 5-apertures
Raw Image
2D FFT
Mask
Electron Beam Reconstruction from a single interferogram.
Results in agreement with other methods
*B. Nikolic, C. Carilli, U. Iriso, N. Thyagarajan, and L. Torino, “Two-dimensional synchrotron beam characterization from a single interferogram“, PRAB, 27, 112802 – Published 25 November, 2024
N=5 apertures
[N(N-1)·2 + 1] peaks
11 distinct peaks

## Slide 12
Example: Beam Coupling Scan
Vertical beam size scan changing the machine coupling with skew magnets.
Results using the NRA mask (7-hole) agrees with:
  Rotating (double aperture) SRI
  LOCO Analysis
The minimum beam size we can achieve at ALBA (11um) is well measured.
U. Iriso, L. Torino, C. Carilli, B. Nikolic, N. Thyagarajn, New interferometric aperture masking technique for full transverse beam characterization, Proc. of IBIC24, 2024

## Slide 13
Example: Real-Time Measurements
Real Time Measurements while varying beam coupling
24h test with different masks (in different days)
*L. Torino, C. Carilli, U. Iriso, B. Nikolic, N. Thyagarajn, Capabilities and limitations of NRA inteferometry for beam size meas, Proc of IPAC26

## Slide 14
SRW Simulations
Alba-II sx
Alba-II sy - depends on Coupling)
For ALBA-II, we plan to use a classical x-ray pinhole camera for normal operation (C=50% coupling)
Nevertheless, for C<10%, the vertical beamsize is dominated by diffraction and the PSF ~ sy
 Synchrotron Radiation Workshop (SRW) simulations have been done, and we have reproduced beamsizes down to 5um*
*L. Torino, C. Carilli, U. Iriso, B. Nikolic, N. Thyagarajn, Capabilities and limitations of NRA inteferometry for beam size meas, Proc of IPAC26

## Slide 15
Other Applications: WaveFront Sensor
1,2,3
    Variations ~ 20o (6nm) are correlated between neighboring holes
𝛅L = 𝛌 x 𝛉i/360o
Gain Phase in Fourier Analysis encode path length diferences 𝛅L
 can be used as WaveFront Sensor

## Slide 16
1-6, 2-5
Before Self-cal
After Self-cal
rms = 28o = 31nm
rms ~ 1.2o = 1.3nm
[𝛔N𝛄 ~ 0.1% ~ 0.4nm]
Mean = static pathlength differences (’metrology’)
Variations (millisec) = vibrations and turbulence
  𝛅𝚽 is correlated between pairs-of-holes => systematic 𝛅L, not noise
  rms after self-cal much lower => measuring frame 𝛅L to high significance
Other Applications: WaveFront Sensor
EXAMPLE APPLICATION:
  Control of possible mirror deformation due to heating, long-term contamination, etc

## Slide 17
Conclusions
New Technique for Full 2D transverse beam characterization from a single interferogram, produced by a multi-hole Non-Redundant Aperture mask.
Advantages wrt “classical” double-aperture :
  Full 2D transverse beam reconstruction  RealTime Measurements of (sx, sy, f)!
  More holes  more light  better SNR, better resolution…
SRW simulations show that measurements down to 5um are possible  ready for ALBA-II
Other benefits:
  Wavefront distortions can be obtained using the Gain Phases: detected tilts ~urad scale
Multi-disciplinary collaboration between Astronomers and Accelerator Physicists pays off!

## Slide 18
extra

## Slide 19
Why Non-Redundant Apertures?
To identify the peaks in the Fourier domain
Baselines with the same distance & direction produce blurring and decoherence in the Fourier space
Redundant combination:
(1,5 – 0,2), Red
(2,5 – 0,1), Black
rms for redundant samples ~6X larger
2D FFT (NRA 5-holes)
Example using a 6-hole Redundant Aperture

## Slide 20
2” input tilt
2.15” fit tilt
Planar fit to the 2” tilt data: measured 2.15” with NRA fitting
Mean (static) residuals ~ +/-10nm
Non-plannar distortions are reproduced between experiments within +/-1nm
Mirror Rotation Tests
Wavefront Sensor “calibrated” using a mirror whose rotation can be controlled down to 0.1urad
Move the mirror by a known amount, and measure the wavefront distortion from the gain phases
APPLICATION:
  Control of possible mirror deformation due to heating, long-term contamination, etc
https://meow.elettra.eu/90/pdf/TUPMO09.pdf
IBIC 2025, TUPMO09
Other Applications: WaveFront Sensor

## Slide 21
Imaging Double-Gaussian Beams
Artificially create beams with different shapes  re-construction using NRA?
Using the Bunch-by-bunch system, we mix different vertical beam sizes within the filling pattern
A. Beam stable (as in Operation):
(sx, sy) = (60, 30)um; f = 8º
(100 bchs of “A” + 340 bchs of “B”):
Beamshape characterization?
B. Coherent Excitation (Qv+Qs):
(sx, sy) = (60, 90)um; f = 12º
Pinhole Image
Pinhole Image
Pinhole Image

## Slide 22
Fit a sum of two Gaussians, with the constraint that their sum of amplitudes is 1
Dual purpose experiment:
  Reproducing non-Gaussian beam shapes
  Possible Halo Measurements: reduction of excited bunches until < 1/440
The complexity of the source that can be derived will depend on the completeness of the u,v sampling.
Mask design should be optimized to reproduce different beam shapes
Imaging Double-Gaussian Beams
https://meow.elettra.eu/90/pdf/TUPMO09.pdf
IBIC 2025, TUPMO09
Amplitude of the two Gaussians (Excited and Non-Excited beams) is compared with the charge ration measured using the Photon Counting.
The beam shape is well reproduced down to ~1% (similar precision obtained with pinhole cameras FE21 & FE34)

## Slide 23
From ALBA to the James Webb Telescope
*C. Carilli, “A New Method for Aperture Masking Interferometric Imaging: Demonstration with the JWST”, Optical Engineering SPIE, 2025
JWST can have up to 18 mirrors (apertures), but one can play with them to produce Aperture Mask Interferometry (AMI).
Self-calibration NRA remains a key capability for imaging at the diffraction limit of the JWST, in particular, for close star-planet systems.
This methodology was long used in radio astronomy, but not, to date, in optical interferometry*.
Interf. NRA with 7-mirrors
Fourier Transform.

## Slide 24
Imaging of dusty binary star WR137
Reliable double-star system image reproduction using self-calibration techniques
Explore other aspects ofthe JWST system  ‘real-time’ wavefront sensor
From ALBA to the James Webb Telescope
’Real-time’wavefront error sensor.
‘standard’ method
(R. Lau et al**)
NRA interf., l=4.8um
(C. Carilli et al*)
NRA interf., l=3.8um
(C. Carilli et al*)
*C. Carilli et al, “A New Method for Aperture Masking Interferometric Imaging: Demonstration with the JWST”
Optical Engineering SPIE, 2025
** R. Lau, et al., “A first look with JWST aperture masking interferometry: dust around the wolf–rayet binary WR 137 beyond the rayleigh limit,” The Astrophysical Journal 963, 127 (2024).

## Slide 25
Publications
https://indico.synchrotron-soleil.fr/event/76/, New interferometric aperture masking technique for full transverse beam characterization using synchrotron radiation, DEELS24, June 2024
https://arxiv.org/abs/2406.02114 , Deriving the size and shape of the ALBA electron beam with optical synchrotron radiation interferometry using aperture masks: technical choices, June 2024
https://opg.optica.org/josaa/abstract.cfm?uri=josaa-41-8-1513 , Laboratory demonstration of image plane self-calibration in interferometry, , Journal of the Optical Society of America , Aug. 2024
https://accelconf.web.cern.ch/ibic2024/doi/jacow-ibic2024-tup56/ , New interferometric aperture masking technique for full transverse beam characterization, IBIC24, Sept. 2024
https://journals.aps.org/prab/abstract/10.1103/PhysRevAccelBeams.27.112802 , Two-dimensional synchrotron beam characterization from a single interferogram, Phys. Rev. Accelerator & Beams, Nov. 2024.
https://opg.optica.org/josaa/abstract.cfm?uri=josaa-42-9-1261, Two-dimensional light beam shape characterization using interferometric closure amplitudes, Journal of the Optical Society of America.
https://arxiv.org/abs/2503.10820 , Self-calibration in two dimensional aperture mask optical interferometry: a new method for wavefront sensing, March 2025
https://meow.elettra.eu/90/pdf/TUPMO09.pdf , Exploiting NRA Interferometry as a Diagnostics Tool for Synchrotron Light Characterization, IBIC25 (2025)
http://dx.doi.org/10.1117/12.3062598 , A new method for wavefront sensing using optical masking interferometry. Proc. SPIE Conference 13619, (18 September 2025);
https://arxiv.org/abs/2510.13502 , A New Method for Aperture Masking Interferometric Imaging: Demonstration with the JWST, submitted to Optical Engineering (SPIE). Oct. 2025
US patent 12,104,901
US patent app. No. 18/878,488
US patent app. No. 19/079,876

## Slide 26
Extra

## Slide 27
Double Aperture Interferometry: Intensity Imbalance
The Visibility V is related to the complex degree of coherence g by a factor involving the intensities going through each hole I1 and I2 .
V =
James Webb Telescope Mask for 7-hole NRA

## Slide 28
2-Hole SRI
3-Hole NRA SRI
5-Hole NRA SRI

## Slide 29
Selfcal Gamp stable ~ 1%
Voltage gains differ by up to 30%
=> Power differs > 50%
1.11
1.23
1.24
1.19
1.19
1.31
1.00
Coherences > 60%
Stable < 1%
Self-calibration Amplitudes = Illumination

## Slide 30: Alternative Techniques for s<5um: NRA Interferometry
*New interferometric aperture masking technique for full transverse beam characterization, L. Torino et al, DEELS’24,
https://indico.synchrotron-soleil.fr/event/76/ – Accepted for publication at PRAB-2024
Non-Redundant Aperture Interferometry using the Visible Light from FE01
Direct measurement of the 2D coherence lenght of the photon beam with one single interferogram
Extract beam sizes (and tilt angle) of the e-beam
NRA Mask:
Direct Interf. Image
FFT Analysis
Electron Beam Image Re-construction

## Slide 31: Alternative Techniques for s<5um: X-ray HNFS
Beam size measurements at NCD down to s = 4.5um