## Slide 1
Bunch cleaning in the booster
Cancellation of beam position oscillations caused by the injection
On behalf of :
M. Dubrulle, A. Franchi, B. Joly, J.M. Koch, T.Perron, E. Plouviez, K. Scheidt
DEELS 15th of June 2015

## Slide 2: THE ESRF STORAGE RING UPGRADE AND THE DIAGNOSTIC GROUP DIAGNOSTIC ACTIVITY
2016: Top up operation will start
Possible following the upgrade of the booster magnet power supplies and the booster RF system
What do we need to make each top up as unnoticeable as possible to the users:
Move the bunch cleaning system from the SR to the booster
Cancellation of the spurious oscillations caused by the injection kickers and septum

## Slide 3: What do we call bunch cleaning?
How to get rid of all the parasitic bunches while keeping untouched the main bunches?
Coming from the linac there is typically a train of one main bunch, 3 bunches with 10-4 to 10-5 lower charge and bunches with about 10-8 lower charge for the rest of the buckets.
The first cells of buncher section of the linac contributes also to the pollution of all the others ideally empty buckets with electrons extracted from their surface by the high accelerating fields
Some users (ID18…) demand 10-8 in the 4 nearest bucket and 2 10-8 integrated on the 992 buckets (not more than one electron/bucket!)
Bucker number:
1
2
3
4
5
6
7
8
9
10
11
scrapper
2.8ns
5mA in a single bunch
=> 15nC
=> 1.1 1011 e-

## Slide 4: Single kick or resonant cleaning?
Beam position at turn n: zn= z0 sin (2puz*n)
Kick at turn n: zn= z0 cos (2puz*n)
We neglect the decoherency due to x
Bunch position
Kick amplitude
Turn number:
1
2
3
4
5
6
7
8
9
10
11
Turn by turn beam position at the cleaning kicker location during a resonant cleaning:

## Slide 5: Cleaning: where to do it ?
Linac gun (90KeV):
Single kick possible. But we will not eliminate some parasitic electrons emitted by the first cells of the linac buncher (=> 10-8 background )
SY booster injection (200MeV):
A fast high voltage pulse generator is needed (single kick)
SY booster (200MeV up to 6GeV, resonant cleaning):
Beam with stable parameters over about only 1ms for resonant cleaning; large transverse size => large scrapper aperture.
SR (resonant cleaning):
Not any longer possible in top up operation:
bad purity during the period between injection and cleaning
Scrapper closing

## Slide 6: Bucket selection: stripline gated shaker setup
beam
H stripline shaker
tune frequency
2 X 100W amplifier
RF synchro
wide band
gating
Bunch selection
X 1
X -1

## Slide 7: cleaning in the booster: it is now mandatory
Results achieved so far:
<3.10-6 one RF period before the main bunch
2.10-4 one RF period after the main bunch
Relative injection in the SR efficiency with SY cleaning ON:
2.10-5 one RF period before the main bunch
2.10-3 one RF period after the main bunch
Bunch purity in the SR after SY cleaning:
<10-10 one RF period before the main bunch
4.10-7 one RF period after the main bunch
4.10-10 two RF periods after the main bunch
But: erratic bursts of badly cleaned injected beams in the SR about every 30 seconds …

## Slide 8: Likely cause of the problem
Phase stability of the 10Hz current driving the SY focusing or defocusing quadrupoles
Solving this problem would involve a major BPSS redesign

## Slide 9
9
12/06/2015
Processing
ESRF Accelerator & Sources Division JM Koch
 FPGA board + CPU module
Booster magnets current measurement (J.M. Koch /PS group)
Analog
front-end
PCIe
FPGA
board
Processor
24 bits
ADCs
3 channels
Towards cleaning device
CPU module
Ethernet
Very accurate DCCTs electronics
3 channels
Cleaning frequency generator
Control
Trigger
Notes: 9
Let’s now come to the correctors , the processor of this module is a powerful FPGA, it will be used:
  As communication node and signal processor:
  this part is real time
  For diagnostic purposes or transfer of parameters through the PCI interface :
  this part is not in real time

## Slide 10
10
12/06/2015
Comparison set-up
 X tune estimation / tune measured on beam
ESRF Accelerator & Sources Division JM Koch
BPSS currents measurement
Tunes estimation from Booster Magnets current
X positions from Beam
(Itech Spark)
I Dipole
I QF
I QD
Trigger
(T0 + 6ms)
BPM
Server
Server
Synchronous
data recording
Notes: 10
Concerning the development, there are a few pieces of code to put together inside the FPGA, data collection from the ADCs converters, the standard access to the PCI express and, of course, the signal processing.
Some interfaces are already existing like the PCIe interface or the interface towards ADCs which will have to be adapted to the ones that will be chosen for this application.
I propose to develop the part using System Generator.

## Slide 11
11
12/06/2015
Comparison result
 X tune estimation / measured on beam
ESRF Accelerator & Sources Division JM Koch
BPSS currents measurement
Notes: 11
Concerning the development, there are a few pieces of code to put together inside the FPGA, data collection from the ADCs converters, the standard access to the PCI express and, of course, the signal processing.
Some interfaces are already existing like the PCIe interface or the interface towards ADCs which will have to be adapted to the ones that will be chosen for this application.
I propose to develop the part using System Generator.

## Slide 12: Cancellation of beam position oscillations caused by the injection
At each injection oscillation of the beam position and orbit distortion in both H and V plane
Amplitude in the horizontal plane plane:
2 mm position oscillation / 7ms damping time
.5mm peak orbit distortion during 2ms
Amplitude in the vertical plane:
.1 mm position oscillation / 7ms damping time
.05mm orbit distortion peak orbit distortion during 2ms
However due to the 103 ratio of horizontal/vertical emitance,
the relative increase of the emitance is much larger in the vertical plane

## Slide 13
Beam orbit perturbation during the injection
Left: H plane Right: V plane (different horizontal and vertical scales)
A mix of septum field leak, injection kickers tilt and non closure of the bump formed by the kicker
2ms
2ms
Non closure of the kickers bump
Septum field leak
Kickers tilt
Septum field leak

## Slide 14: Injection components
The injection kick path includes sextupoles =>
the kicker bump is not closed during the kick rise time and fall time
septum
Injected beam path
Stored beam path
kickers

## Slide 15: kickers pulse shape

## Slide 16: Parasitic kicks shape
Cyan: kickers pulse shape
Magenta: shape of the parasitic kicks due to non closure of the bump
2.8 ms

## Slide 17: How are we going to adress the problem:
Septum leakage:
less than 1KHz BW, repetitive shape perturbation
Solution:
Use fast correction magnet driven by a pulse generated by an arbitrary signal generator triggered by the septum signal
Kikers tilt:
Tilt evaluation derived from turn by turn H and V position measurements
Suppression of the tilt by a realignement of the kickers
Non closure of the horizontal injection bump:
more difficult…
Why do the FOC and bunch by bunch feedback cannot take care of it?

## Slide 18: Back to the cleaning in the SR
Feedback system
Random perturbation
Correction signal derived in real time of the
measurement of the beam parameter perturbation
Drawback:
the loop cut off frequency is limited to about 10% of the loop components bandwidth

## Slide 19: Back to the cleaning in the SR
Feedforward scheme:
More efficient use of the corrector :
the full bandwidth of the corrector can be used without stability problem
Repetitive perturbation
Correction signal generated using the lookup table
Injection trigger
Perturbation
recorded offline
Generation of the correction
signal lookup table

## Slide 20: Fast correctors for the suppression of the injection related perturbations
Injected beam path
Stored beam path
H and V fast correctors
(of the old FOC system)
1MHz BW shaker

## Slide 21: Suppression of the horizontal orbit distortion due to the septum field leak
Using one of the horizontal fast orbit correctors, driven by an arbitrary shape signal generator, the suppression of the effect of the septum leak is very effective (right plot)
2ms
Non closure of the kickers bump
Septum field leak
Non closure of the kickers bump is the only effect remaining

## Slide 22: H kicker bump non closure: measured orbit distortion
3 turns

## Slide 23: Effect of the kicks in the sextupoles
Perfect compensation: technically very demanding…
First sextupole
Second sextupole
Compensation kicker
Bandwidth:
original kicks: about .5 MHz (pulser and ceramic coating thickness)
Sextupoles effect: quadratic effect => bandwidth doubled…
Perfect compensation:
Two parabolic shaped kicks of 1ms separated by 1ms;
Several KV, >102A pulser

## Slide 24: Turn by turn change of the beam position at the shaker location
Beam position at turn n: zn= z0 sin (2puz*n)
Kick at turn n: zn= z0 cos (2puz*n)
We neglect the decoherency due to x
Bunch position
Kick amplitude
Turn number:
1
2
3
4
5
6
7
8
9
10
11
Easier: damping over several turns:

## Slide 25: SHAKER FOR THE APPLICATION OF MULTITURN KICKS
Magnetic shaker:
6 coils
Bandwidth is 1MHz
Driven by a 700 Watts amplifier
9 turns pulse shape generated by an arbitrary waveform signal generator

## Slide 26: Effect of the horizontal oscillation damping
2ms
Right plot: the oscillation is reduced to a bit less than 50% of the initial amplitude
after 9 turns instead of 7 ms…

## Slide 27: Vertical oscillation due to the tilt of the kickers
Work in progress (A. Franchi)
Record the turn by turn H and V position
after the firing of the injection bump
main hamonic at Qx=.44
main hamonic at Qx=.39

## Slide 28: Vertical oscillation due to the tilt of the kickers
Work in progress (A. Franchi)
main hamonic at Qx=.44
main hamonic at Qx=.39
Record the turn by turn H and V position
after the firing of K1,K2,K3,K4
Do a fft analysis to find the tilt of the kickers;
Derive the correction tilt on K2 and K3 which will cancel the oscillation recorded after the firing of the injection bump…
Looks straightforward but it is not!
We have not yet found the right K2 and K3 tilt

## Slide 29: Conclusion
A lot of this project is still a work in progress:
Booster cleaning:
Improve the integration of diagnostics to the system (synchronous monitoring at the injection rate of the tune and BPSS currents)
Horizontal oscillation damping:
Implement the control to make it usable in operation
Vertical kickers tilt:
during 2015, implement a remote control of the kickers tilt
Septum fields leak compensation:
Add the vertical correctors to the set up; implement the control to make it usable in operation

## Slide 30: ID24 detectors principLe
Particularly sensitive to the horizontal beam position stability…

## Slide 31: Perturbation caused by the injection
Blue dots: no kickers compensation
Red dots: compensation active

## Slide 32: Thank you for your attention