## Slide 1: LOREA: the new ARPES beamline at ALBA for Band structure in complex materials
Massimo Tallarida, Federico Bisti, Debora Pierucci
24.02.2020

## Slide 2: LOREA for band structure of complex materials
Quantum materials for spin-charge conversion
Surface vs bulk states
e-ph interaction
correlations
Dirac cones
Fermi arcs
Rashba effect
Band gap
Band alignment

## Slide 3: The optical design of LOREA
Flux ~ 1012 ph. @max resolution
Energy Range 10-1000eV with resolution > 104
Beam spot of the order of 10µm

## Slide 4: The end-station for LOREA
MBS A-1_#0004@Saga University Synchrotron Light Application Centre
Bi (111) Data taken by Dr. M.Imamura, Prof. K. Takahashi
Specifications
Analyzer:
ΔE ~1 meV @ 20 eV.
Δθ < 0.1°
±3.5° ±7° ±15° 2D modes

## Slide 5: The end-station for LOREA
Entrance Slit
from F. Bisti
Sample
hν
e-
Spin up
Spin down
MCP
O/Fe(100)
Magnetizing coil
Ekin=6 eV
Aperture for spin detection
Upgrade to spin-resolved ARPES: VLEED seems the best option
MBS A-1_#0004@Saga University Synchrotron Light Application Centre
Bi (111) Data taken by Dr. M.Imamura, Prof. K. Takahashi

## Slide 6: The end-station for LOREA
Photon beam
Preparation Chamber
Load lock
Atomic Layer Deposition
Organic Molecules Chamber
Samples storage + UHV suitcase
Specifications
Analyzer: Manipulator:
ΔE ~1 meV @ 20 eV. 6-axes fully motorized
Δθ < 0.1° T < 10 K
±3.5° ±7° ±15° 2D modes Up to 4 electrical contacts
Spin detector
(upgrade in 2021)

## Slide 7: LOREA for band structure of complex materials
Quantum materials for spin-charge conversion
Ag/Bi (Sb) interfaces
LAO/STO
TMD Gr (2D systems)
Bi2Se3
Phosphorene
a-Sn
Weyl Semimetals
SmB6 - Kondo Insulator

## Slide 8: Conclusions and acknowledgments
The new ARPES beamline at ALBA is on the way
A good opportunity for the Spanish ARPES community to grow and improve the technical capabilities
Low T, High resolution, wide energy range, 2D measurements, automatization, wide variety of sample preparation tools,…
This project is co-funded by the European Regional Development Fund (ERDF) within the Framework of the Smart Growth Operative Programme 2014-2020

## Slide 9: Conclusions and acknowledgments
This project is co-funded by the European Regional Development Fund (ERDF) within the Framework of the Smart Growth Operative Programme 2014-2020
All ALBA staff for the technical support
Engineering Division: Alejandro Crisol (mechanical design of LOREA and Monochromator); Llibert Ribó (monochromator mirrors), Nahikari Gonzalez, and Joaquín González (NanoBender); Raquel Monge (Vacuum group), Marta Llonch (Alignment), Nuria Martí and Cristina Orozco (Infrastructures), Carles Colldelram, José Ferrer
Computing Division: Bernat Molas (Electronics), Fulvio Becheri (Control System), Jorge Villanueva (Protection Systems), Sergi Pusó (IT), Guifré Cuní, Toni Pérez, Oscar Matilla
Accelerator Division: Pep Campmany (ID), Jordi Marcos (FE), Montse Pont (installations), Francis Pérez
Administration: Vanesa Faro, Edgar Aigner
Debora Pierucci and Federico Bisti (LOREA Group)
Josep Nicolás (Optical design and Project Executive)