## Slide 1: µCT at ALBA: status and vision
Alberto Mittone
8/9.11.2021
Structural Cell and Tissue Section Review The Existing Tools
Notes: FAXTOR is a new beamline dedicated to fast hard x-ray computed tomography imaging currently under construction at ALBA.

## Slide 2: FAXTOR - BL31 Staff
Current FAXTOR staff:
Alberto Mittone (BL responsible)
Since Feb 2019 – X-ray imaging/Bio/software
Alessandra Patera (BL scientist)
Starting date January 2022
X-ray imaging/Mat science
To be HIRED ~ 2022 (BL scientist)
To be HIRED ~ 2024 (Post-doc)
Foreseen position plan:
4 “structural positions” (long term guaranteed).
  3 scientists
  1 post doc position
?
?
“Matrix” staff:
Llibert Ribó
Mechanical engineer
Commissioning starts – mid 2023
TBR
Controls engineer
Álvaro Baucells
Electronic engineer
?
Joint efforts with MX beamline (XAIRA) to establish a High throughput data infrastructure
+ work package managers (Infrastructure, ID, FE, Vacuum, Computing…)
Notes: Consider NANO branch in triangle and its position
High energy mark -
Add triangle / energy / time resolution / energy resolution + keyword application
Access higher
Moving into the GAP analysis, specific know-how and the development of equipment will be required for in-situ/in-operando studies but this can be achieved through in-house projects and external partnerships. The complex scientific projects can be sustained by coupling them with new services and structure techniques. Heavy computation services will be required, so a close collaboration with data analysis services is required. The limitations in spatial coherence can be smoothed by implementing at ALVA of a mini-beta section and in the future with the ALBA2 storage ring upgrade. The last point is linked to the limited multi-scale capabilities, however this gap can be filled if it is considered in the framework of ALBA2 a physical extension of the beamline or the construction of a complementary long high energy imaging beamline.

## Slide 3: FAXTOR - Beamline and instrumentation
ID Source: Multi-pole wiggler
2.5 T peak field/5 poles/In vacuum
Energy range: 10 – 70 keV
Max beam size @sample: 35x12 mm2 (HxV)
Flux: ~6*1013 ph/s/0.1%BW - 30 keV/250 mA
@ENDSTATION: Filtered white beam or Double Multilayer Monochromator ΔE/E ~ [2,5]% beam
MPW54
DMM
Filters
CT-stage
36 m
20 m
18 m
Detector
36-40 m
Temporal resolution:
100 ms - 1000 s (CT)
100 µs - 1 s (Radiography)
Operational to users - Beginning 2024
FAXTOR
End-station
Pixel size: 1-10 µm
Field of view: few mm to few cm
Spatial resolution
Two detection stages
10-50 keV
In construction
Notes: The beamline is fed by a short in-vacuum multipole wiggler, currently under construction. This provides a broad energy spectrum, ranging between 10 keV and 70 keV (in filtered white beam). The main Optical element of the beamline is a Double Multilayer Monochromator, providing an energy bandwidth comprised between 2% and 5% in range between 8 keV and 50 keV.

## Slide 4: FAXTOR - Techniques and science
Available techniques:
Propagation based imaging. (1-5 µm, 10-40 keV)
X-ray absorption imaging. (1-10 µm, 10-70 keV)
Time resolved radiography.
µ-Computed tomography (3D/4D).
+ Combination with external stimuli
land
Romano M. et al. Cancers, 2021.
µCT/µXRF/SAXS/WAXS
Stroebel J. et al. Sci. Rep, 2020.
Mittone A. et Al, JSR 2020.
Rack A. et al. Instruments, 2020.
Cartilage imaging (human plugs)
Rat livers
Neuroimaging – spinal cords
Rat brains
Notes: As techniques propagation based X-ray phase-contrast and absorption-based imaging will be used on a daily basis. Future extensions including differential phase-contrast imaging can be also foreseen. Different acquisition protocols will be available, from time resolved projection imaging, to static and time resolved computed tomography.

## Slide 5: SWOT
Strengths
Threats
Weaknesses
Opportunities
No in-vivo measurements capabilities (small animals).
Limited sensitivity in phase-contrast (Spatial coherence).
Limited spatial multi-scale capabilities.
Not yet established users community.
Reduced horizontal electron beam size with ALBA2.
IT Infrastructure upgrade, creation of computing and data analysis unit.
Long shutdown (machines upgrade) in other facilities.
Flexible End-station (in-situ/in-operando capabilities).
Broad energy range with Tunable spectrum.
Broad time resolution.
ALBA2 long shutdown during possible ramping up of user community.
Competing communities at the beamline (Bio / Mat. science).
Competitive environment in Europe.
Notes: Check shutdown/list of competitors (last point of opportunity)
Easy setup change (mono/filtered white beam):
Concerning the SWOT analysis, the identified beamline strengths are a flexible end-station, easy change of the setups and broad energy range. As weaknesses the BL is currently in construction and in Europe a competitive environment is present in the field. In addition, strong computation requirements are required and currently optimal commercially available solution of high speed streaming CMOS camera are lacking. One last issue is linked to the limited of spatial coherence achievable. The main threats are linked to possible lack of computing resources, the evolution of competing imaging techniques and technical upgrades of existing beamlines and storage rings. As opportunities we will take advantage of the IT infrastructure upgrades, and the performance improvement expected from the ALBA 2 machine. In addition, a strong industrial interested arose around FAXTOR is present.
THREATS:
ALTERNATIVE TECHNIQUES: SHANEL - OPTICAL CLEARING
Conventional source developments -> larger photon fluxes

## Slide 6: GAP analysis
Gap
Mitigation
Coupling with Data Analysis Services. IT infrastructure upgrades.
Ongoing tests on the implementation of a mini-beta section/ALBA2 machine.
Implementation of differential phase-contrast imaging setups.
Early dissemination/establishing collaborations.
Heavy computational services Required.
Limited phase-contrast sensitivity.
Not yet established users community.
Limited multimodal capabilities.
Implementation of new instruments enabling multimodal approaches.

## Slide 7: Integrating µCT into multimodal experiments
Cryo-SXT
FTIR
Pixel size
Sample size
50 µm
5 µm
100 nm
>10 cm
~ 2 cm
~ 200 µm
Pérez-Berná A. et al, acsNANO, 2016.
Brandlhuber M. Inv Rad, 2016.
µCT
1 µm
10 µm
LeNaour F. Anal Chem, 2012.

## Slide 8
Towards high energies?
Gasilov S. et al. BOE, 2013.
Walsh C. et al. Nature Met, 2021.
L. Fardin et al. Sci Rep, 2021.
Larger/denser samples.
Low dose/in-vivo applications.
A. Horng et al. Inv Rad, 2014.
Requires ID source.
ALBA disadvantage compared to High Energy machines.
In-vivo user community is limited.
Full human knee joint
Multiscale imaging of organs
Ex-vivo Breast imaging
In-vivo lung imaging

## Slide 9
Mind the gap!
A. Cedola et al. X-Ray Phase Contrast Tomography Reveals Early Vascular Alterations and Neuronal Loss in a Multiple Sclerosis Model. Sci. Rep. 2017.
µCT
Sub µCT
I. Bukreeva et al. Quantitative 3D investigation of Neuronal network in mouse spinal cord model. Sci. Rep. 2017.
Expanding multi-scale capabilities - sub-µm CT (spatial resolution)
A. Horng et al. Multiscale X-ray phase contrast imaging of human cartilage for investigating osteoarthritis formation. J. Biomed. Sci, 2021.
Sub µCT
µCT

## Slide 10: Hard X-ray CT Vision
High energies (>50 keV)
Spatial resolution
Chemical
sensitivity
Time resolution
µ-XRF
µ-XANES
FAXTOR
µ-CT
FAXTOR @ALBA2
Spatial coherence
Long High energy BL
Sub µ-CT
 | Sub-mm CT | HE CT in vivo
 | Hard X-rays | Hard X-rays
 | SB/W | W
 | 10-30 keV | 50-120 keV
 | <1 µm | 10 - 50 µm
Near Native |  | 
Multimodal |  | 
Dynamics |  | 
Strong Community |  | 
Proposed |  | 
4th generation upgrade
3th generation upgrade
Essential tool
Desirable tool
Capability
Disregarded tool
NA
!

## Slide 11: Thank you for your attention!